## Slide 1: Kendrick Street Bicycle Boulevard Final Design
Northern Arizona Transportation Services
Stephen Hirte
Yousef Alkandari
P.J. McKelvey
Christopher Sobie
April 24th, 2015

## Slide 2: Project Personnel
Project Manager – Christopher Sobie
Software Lead – Pierce-Jon McKelvey
Research Lead – Stephen Hirte
Site Lead – Yousef Alkandari
Alkandari 2
Northern Arizona Transportation Services Team Members [1]

## Slide 3
Clients
  Jeffrey Bauman, PE, City of Flagstaff Traffic Engineer
  Martin Ince, PE, City of Flagstaff Multimodal Planner
Technical Advisor
  Jeffrey Bauman, PE, City of Flagstaff Traffic Engineer
Stakeholders
  City of Flagstaff - Owner
  Local and National Cyclists
  Flagstaff High School
  Flagstaff Community
  Cities who desire a bicycle boulevard
Alkandari 3
Stakeholders

## Slide 4
Convert Kendrick Street into a Bicycle Boulevard
Improve bicycle safety and circulation by:
  Creating low traffic volumes
  Discouraging non-local motor vehicle traffic
  Provide free flow travel for bicycles
  Creating distinctive look or ambiance
Accomplished by:
  Equal priority among users
  Pavement markings
  Eliminating stops
  Unique branding
Unique Branding for WI Bike Boulevard [2]
Sobie 4
Project description

## Slide 5
Citywide View [3]
Local View [3]
Sobie 5
Project Location

## Slide 6
FUTS connection
  City-wide network of non-motorized shared-use pathways used for recreation and transportation
Unmarked cross-section (37 feet min.)
Street parking
Non-free flow
Moderate to poor pavement condition
FUTS Trail Connection on northern end [4]
FUTS Trail connection on southern end [4]
Sobie 6
Existing conditions

## Slide 7
Existing Traffic Control [3]
Typical cross-section of Kendrick Street [4]
Cyclist on sidewalk and random street parking [4]
Karen Cooper Trail
Sobie 7
Existing conditions

## Slide 8
Kendrick Street Project Limits
Downtown FUTS Concept Plan [5]
Sobie 8
Future plan for futs trail

## Slide 9
National Association of City Transportation Officials (NACTO)
  Bicycle boulevard design elements (nationally)
  Route planning, signs and pavement markings, speed and volume management, street crossings, green infrastructure
Manual on Uniform and Traffic Control Devices
AASHTO Geometric Design Guide
  National codes and standards for all road components
Arizona Department of Transportation / Flagstaff
  Local State and City standards
NACTO Urban Bikeway Design Guide
MUTCD / AASHTO Geometric Design Guide
ADOT Design Manual
Sobie 9
Project methods

## Slide 10: Data Collection/Results – Vehicle Speeds
26 mph
26 mph
Hunt Ave
Fine Ave
Elm Ave
Dale Ave
Cherry Ave
Birch Ave
Kendrick St
26 mph
27 mph
24 mph
22 mph
22 mph
17 mph
17 mph
20 mph
23 mph
28 mph
85th Percentile Speeds for Vehicle in Project Area [3]
Hirte 10

## Slide 11: Data Collection/Results – ADT
26 mph
26 mph
Hunt Ave
Fine Ave
Elm Ave
Dale Ave
Cherry Ave
Birch Ave
Kendrick St
818
807
244
729
89
207
210
927
258
647
1515
232
1065
Average Daily Traffic for Vehicles in Project Area [3]
Hirte 11

## Slide 12
Community project. Input matters!
9 question survey using SurveyMonkey.com
  66 respondents of varying age and riding ability
Hand out fliers to cyclists / windshields
Attend Flagstaff Bicycle Advisory Committee Meetings
Attend Flagstaff Transportation Committee Meeting
Successful Flagstaff Community Bicycling Project [6]
Hirte 12
Community involvement

## Slide 13
Chart: Current Usage
| Never, not my route | Never, not safe | Sometimes | Often | Daily
 | 0.1515 | 0.0152 | 0.2727 | 0.3788 | 0.1818
Chart: Potential Usage
| No effect, already bike daily | No effect, not my route | No effect, I do not bike | I would bike more | I would bike a lot more
 | 0.2308 | 0.1538 | 0.0308 | 0.3692 | 0.2154
Chart: Motorist Comfort Level
| Uncomfortable | Somewhat Comfortable | Comfortable
 | 0.2308 | 0.1538 | 0.0308
Chart: Cyclist Comfort Level
| I do not ride there | Not Safe | Somewhat Safe | Very Safe
 | 0.0455 | 0.3333 | 0.5455 | 0.0758
Hirte 13
Survey results

## Slide 14
Positive Feedback
  “As a resident of N Kendrick St. I would like to see a bike boulevard, not only for the safety of bikes but to preserve the street as a non-major alternative thoroughfare to Humphreys. There is a LOT of foot and bike traffic on Kendrick.”
  “I encourage any forward progress in improving and promoting bike transportation in flagstaff, regardless if it benefits my route.”
Negative Feedback
  “Motorist support for increased/improved bicycle facilities will not increase until bicyclist are taxed to pay for those facilities.”
  “Of all the things to spend tax dollars on, are you serious? Help me understand how unequal tax dollar input from cyclists warrants the massive tax dollar output from people driving cars.”
Hirte 14
Survey Comments

## Slide 15
Minimize implementation costs
Maximize safety
NACTO Recommendations for Bike Boulevards
  Less then 3000 ADT
  85th Percentile speed of 25 mph or less
Minimize residential impact
Designed for minimum cross-section (37 ft)
Unique marking on Bicycle Boulevard in Columbus, OH [7]
Mckelvey 15
Design constraints and criteria

## Slide 16
Alternative 1 Drawing [8]
Alternative 1
Alternative 2
Alternative 2 Drawing [8]
Mckelvey 16
Preliminary alternatives
Notes: Negatives:
  Center stripe discourages drivers from passing bicycles (frustration / lack of respect)
  More striping = higher cost
Negatives:
  Center striping
  Discourages Respect
  More striping = higher cost
  Eliminates parking

## Slide 17
Two 7 ft parking lanes
  MUCTD minimum
23 ft travel way
  NACTO minimum
No centerline stripe
  Preferred by NACTO
  Easier time passing
Positives:
  Most cost efficient
  Inviting to all users
  Creates respect among all users
  Can use unique pavement markings
Preferred Alternative Drawing [8]
Alternative 3
Mckelvey 17
Proposed design

## Slide 18
Eliminate stop signs along route
  Stops increase delay and encourage low compliance
Maintain bicycle boulevard conditions
  Eliminate / manage new cut through motorists
  Lower traffic speeds and volumes
  Bulb-out treatments – narrow travel way
  Striping instead of curb and gutter
Addition of crosswalks
25 mph Speed Tables
  3 along Kendrick St
Example: Bulb-outs from NACTO Design Guide [9]
Mckelvey 18
Design elements
Common Speed Table Dimensions [10]

## Slide 19
Wayfinding, signage, and pavement markings
  Provide photographic uniqueness for bicycle boulevard
  Differentiate from other local streets
  Raise awareness of designation
  Prompt motorists to look for cyclists
Unique Kendrick Street Roadway Sign [8]
Kendrick Street Pavement Marking [8]
Mckelvey 19
Design elements - wayfinding

## Slide 20
Intersection of Kendrick Street and Dale Street with new crosswalks, pavement markings, and bulb outs. [8]
Mckelvey 20
Design elements – geometric

## Slide 21
Project Hours |  |  | 
Christopher Sobie |  |  | 140
Pierce-Jon Mckelvey |  |  | 116
Yousef Alkandari |  |  | 104
Stephen Hirte |  |  | 140
Total hours |  |  | 500
Total Project Cost |  |  |  | 
Items | Units | Unit Cost | Amount | Cost
Parking Striping | LF | $0.70 | 400 | $280
Speed Table | EA | $2,500 | 3 | $7,500
Boulevard Striping | EA | $350 | 23 | $8,050
Thermoplastic | SF | $13 | 1540 | $20,020
Boulevard Signage | EA | $200 | 12 | $2,400
Advance Signage | EA | $200 | 12 | $2,400
Speed Table Signage | EA | $200 | 6 | $1,200
R1-1 Signage Reuse | EA | $100 | 4 | $400
 |  | Implementation Cost |  | $42,000
 |  | Administrative Cost |  | $43,000
 |  | Grand Total |  | $85,000
*Costs of implementation _includes materials, _installations, and man _hours.
Alkandari 21
Project hours and costs

## Slide 22
Economic
  Less pavement rehabilitation
Societal and Cultural
  Increased in local cyclists
  Aesthetics and community
Environmental
  Fewer greenhouse gas emissions
Health
  Biking is good exercise
  Promotes a healthier community
Global
  Paves the way for future bike boulevards nationally and internationally
Alkandari 22
Cyclists of all levels enjoying bicycle boulevard [7]
Broader impacts of design

## Slide 23
Martin Ince, City of Flagstaff Multimodal Planer
Jeff Bauman, City of Flagstaff Traffic Engineer
Logan Couch, City of Flagstaff Traffic Intern
John Koch, Ennis-Flint Traffic Patterns
National Association of City Transportation Officials
Alkandari 23
acknowledgments

## Slide 24
[1] Photo Credit: Katherine Dean
[2] "Review: Wisconsin's First Bicycle Boulevard." Over the Bars in Wisconsin. N.p., 02 Sept. 2010. Web. 10 Mar. 2015.
[3] Google Earth Pro (2011), Version 6.1 (Software), Available from http://www.google.com/enterprise/earthmaps/earthpro.html
[4] Photo Credit: Christopher Sobie
[5] Plan provided by Martin Ince, City of Flagstaff Multimodal Planner
[6] Welcome to an Engaged Community. (n.d.). Retrieved September 18, 2014, from https://az- flagstaff3.civicplus.com/index.aspx?nid=1379
[7] "First Signs of the New Milton Ave. Bike Boulevard!!" ColumbusUnderground.com. N.p., 03 Oct. 2008. Web. 10 Mar. 2015.
[8] AutoCAD Civil 3D. Vers. J.104.0.0. USA: Autodesk, 2014 Project costs
[9] Urban Bikeway Design Guide. New York: National Association of City Transportation Officials, 2012. Print. Final Report
[10] http://www.ladpw.org/Traffic/NTMP/speed-table.gif
Alkandari 23
References

## Slide 25
"Confusing Traffic Signs." A Fun Blog. N.p., 21 July 2014. Web. 10 Mar. 2015.
Questions?