## Slide 1: PCI- BIG BEAM CONTEST
Deena Albustan
Eman Albdiywi
Nicholas Jokerst
Michael O'Reilly

## Slide 2: INTRODUCTION
PCI: Pre-stress Concrete Institute
  Big Beam Contest
  Design and produce a PCI beam
Design Constrains
  Beam spans 17 ft.
  No cracks in beam before 18.75 kip.
  Beam should fail between 30 to 37 kip.
Design Criteria
  Total Cost, Overall Weight & Ultimate Deflection
Figure 1: PCI Logo
Figure 2: TPAC Logo
(Project Sponsor and Producer)
Notes: Eman 30-60 seconds

## Slide 3: PCI BIG BEAM MATERIALS
1. add the costing of beam from rules
2. Content: discuss what materials we could/couldn’t use and the methodology I took to get the cheapest beam
Figure 3: PCI Big Beam Materials and Costs
Notes: Eman: 30-60 seconds

## Slide 4: TPAC LIGHTWEIGHT CONCRETE MIX
Figure 4: TPAC LW Concrete Mix Strength
Figure 5: TPAC LW Concrete Mix Ticket
Table 1: Concrete Mix Comparisons
Notes: Eman
Pros: 1. Low Unit weight2. Partiially air entrained, reduces cracking with severe temperature changes3.Good to above average 28 day compression strength for lightweight (6,500 psi anticipated)4. Dry Unit weight @ 28 day pobably between 120-122 pcf5. Low water cement ratio assist with permeability6. Easy to place concrete with maximum consolidation7. Architectural Finish8. High fire rating
Cons: 1. Low shear values @ transfer and 28 days2. Specific gravity of lightweight material is unstable3. Low transfer strengths if proper curing procedures are not used4. Air entrainment is variable based on temperatures (air and Ambient)5. Very Rocky Finish on the top, sometimes undesirable6. Concrete has to be batched under strict supervision

## Slide 5: BEAM ANALYSIS
Steps to check the design performance:
Verify Pre-stress < allowable
Check (Pcr)
Check
Check (Pult) between (30 – 37) Kips
Figure 6: Wide Flange Beam Cross Section
Figure 7: MathCAD Analysis
Table 2: MathCAD Variable
Notes: Remind class about this slide and that this is exactly a snapshot of what weve been doing for two weeks but we each chose a separate criteria to design our beams…transition into and “and here are our results”

## Slide 6: BEAM SCORING
Points =
Figure 9: Beam Scoring Table
Table 3: Competition Scoring

## Slide 7: RESPONSE 2000 ANALYSIS
Figure 8: RESPONSE Input
Figure 9: Cracked Section
Figure 10: Predicted Stress-Strain curve
Mult= 138.4 kip-ft =
Pult = 36.6 kips

## Slide 8: NAU 2016 PCI Big Beam Design
Figure 12: NAU Big Beam Bill of Material
Figure 11: NAU Big Beam Cross Section

## Slide 9: TPAC PRODUCTION DAY
Figure 13: Formwork and Rebar
Figure 14: Rebar Spacing
Figure 15: Concrete Pour
Figure 16: Complete Beam Pour

## Slide 10: CYLINDER TESTING
Figure 17: Compression Test
Figure 18: Split (Tensile) Test
Average Compressive Strength (23 day): 7365 psi
Average Tensile Strength (23 day): 369 psi

## Slide 11: BIG BEAM TEST SET UP
Figure 19: Conceptual Set-Up Diagram

## Slide 12: BIG BEAM TESTING
Figure 20: Shortened Competition Video

## Slide 13: BEAM PREDICTIONS VS. RESULTS
Chart: Load vs Deflection
Figure 21: Load vs. Deflection
Table 4: Final Prediction and Result Comparison

## Slide 14: BEAM AUTOPSY
Figure 22: Failure Plan View
Figure 23: Failure Top View
Figure 24: Exposed Compression Steel

## Slide 15: SCHEDULE COMPARISON
Scheduling Complications:
RESPONSE software tutorials
TPAC internal scheduling
Concrete Curing
Table 5: Project Schedule

## Slide 16: PROJECT HOURS
Total Projected: 629 hrs.
Actual: 522 hrs.
Table 5: Projected vs. Actual Hours

## Slide 17: PROJECT COST COMPARISON
Actual Project Cost |  |  |  | 
1.0 Personnel | Classification | Hours | Rate, $/hr | Cost, $
 | SENG | 129 | 175 | 22,575.00
 | ENG | 135 | 75 | 10,125.00
 | AA | 114 | 60 | 6,840.00
 | INT | 144 | 50 | + 7,200.00
 | Total |  |  | = $46,740
2.0 Travel | 2 trips to Phoenix at 286 mi/trip | $0.445 per mile |  | + $254.00
3.0 Project Total |  |  |  | = $46,994
Table 6: Projected Design Costs
Table 7: Actual Design Costs
Total Projected Cost |  |  |  | 
1.0 Personnel | Classification | Hours | Rate, $/hr | Cost, $
 | SENG | 153 | 175 | 26,775.00
 | ENG | 169 | 75 | 12,675.00
 | AA | 95 | 60 | 5,700.00
 | INT | 197 | 50 | + 9,850.00
 | Total |  |  | = $55,000
2.0 Travel | 2 trips to Phoenix at 286 mi/trip | $0.445 per mile |  | + $254.00
3.0 Project Total |  |  |  | = $55,254.00

## Slide 18: IMPACTS OF PRESTRESSED CONCRETE
University Impacts:
Improved Design Standards for future NAU Teams
Public recognition for the NAU CEFNS Department
Broader Impacts:
Concrete production results in high C02 release
Demolition of aged concrete buildings releases ad-mixtures
Prestressed beams decreases build time
Prestressed camber allows for higher deflections before failure

## Slide 19: THANK YOU!
Acknowledgements:
  Robin Tuchscherer, P.E., PhD
  TPAC Arizona
    Abdul Kassab and Vince Rossi
  Prestressed Concrete Institute