## Slide 1
Team Members: Breanna Smith, Meshal Alotaiby, Verneon Reed, Alex Goodman, Jonathan Melendez, Yiyang Chen and Yuliang Wang
Photograph Provided by: Jonathan Melendez
PEACH SPRINGS OVERPASS AND GRADE SEPARATION

## Slide 2: Project Overview
Peach Springs, AZ
Performing a grade separation for an existing at grade road crossing with the railroad
Prior to the fall semester the project was divided into two teams: Grade separation and structural
Issues with current design:
  Safety
  Noise complaint
  Emergency Vehicle access
Photograph Provided by: National Online Project

## Slide 3: Project Details
Clients:
  Julie Alpert- Transportation Planner Hualapai Tribe, Public Services Department
  Kevin Davidson- Hualapai Tribe Planning & Economic Development Director
  Philip Wisely PE- Public Services Director
Technical Advisor
  John Tingerthal, MSCE, EdD, PE
Advisor
  Wilbert Odem, PhD PE
Photograph Provided by: Google SketchUP

## Slide 4: Environmental Analysis
Photograph Provided by: www.defenders.org
Overview phase: To determine the specific presence/absence of projected species
Design phase: To protect wildlife from roadway traffic and to allow for the safe wildlife movement across the study area.
Construction phase: To protect all environmentally sensitive species in the area during the construction phase.
  Black footed Ferret
Photograph Provided by http://davesgarden.com/
Grand Canyon beavertail cactus
Grand Canyon Cottontop Cactus
Photograph Provided by http://www.florafinder.com/
Varied fishhook cactus
Photograph Provided by http://www.britannica.com/
Notes: Prior to construction the region must be checked, if any homes or vegetation of the noted endangered species are found, it must be properly handled by the wildlife foundation and the Haulapai nation. Is there anything else we would do to protect the vegetation and black footed ferret

## Slide 5: Traffic Analysis
Diamond Creek Rd and BNSF Crossing:
  106 cars/day
  38 people/day
  86 trains/day
Diamond Creek Rd
  2 lane Highway and 1 lane in each direction.
ADOT Class 3
  Highway serving moderately developed areas.
Photograph Provided by: www.google/maps
Intersection
Diamond Creek Rd.
BNSF Railroad
Notes: Remove Percentages and Provide actual values. Where did the class III come from and what exactly does it mean? Use less words

## Slide 6: Determining Level Of Service (LOS)
Criteria:
  Free Flow Speed ( FFS ) = 47
  Width Lane = 11 ft.
  Shoulder Lane = 2 ft.
  Peak Hour Factor ( PHF ) = 0.9
  Demand Volume = 4.42 Veh/hr.
  Access point/mile = 40
  Terrain ( Level )
  Where:
    = Average Traffic Speed
    FFS= Free Flow Speed
    PHF= Peak Hour Factor
    PFFS= Percent Free Flow Speed
    = Analysis flow rate in analysis direction
    = Analysis flow rate in opposing direction
Notes: Give more detail and mention the names of equations What does the level of service actually mean? Correct the values to provide an accurate LOS (Should be A)/ Might need multiple slides for this equation?

## Slide 7: Cont... Determining LOS
= 47 – 0.00776 (106+106) - 1.8 = 43.55488 mph
PFFS = = (43.55488/47) = 0.926 = 92.6%
Since PFFS = 92.6% , LOS = A
One lane Road
Photograph Provided by: Google SketchUP

## Slide 8: Speed Limit
Speed Limit
  The speed limit determined for the overpass was 35 mph
  This was based off the speed limit in AZ-66
  Since the requirement for an urban highway is 30-50 mph we can confirm that our design speed limit complies with ADOT requirements
Equation for Maximum Speed Limit
  Less than 55 mph (90 km/h), V=6S
  V = Speed Limit (mph)
  S = The maximum distance between two speed limit signs (miles)
  35 mph = 6S
  S = 35/6 = 5.83 miles
Photograph Provided By: streetsignusa.com

## Slide 9: Geotechnical Analysis
A geotechnical report was used to approximate soil conditions on site.
Subsurface soils:
  clayey sand with gravel down to a depth of about 7 ft and silty sand below that.
Low plasticity
The density of the soil is loose and is consolidate under a foundation load.
Engineered fill is recommended for construction.
Photograph Provided By: Hualapai Cultural Center Soils Report
Notes: Provide more detail/ Highlight result

## Slide 10: Hydrologic Analysis – Rational Method
The Mohave County Drainage Design Manual: Rational Method.
C = runoff coefficient based on land use.
i = rainfall intensity from NOAA-14 data.
A = area
The DDMSW software developed specifically for Mohave County by KVL Consultants, Inc. was used to complete this analysis.
50 year storm output from Drainage Design Management System for Windows (DDMSW)
Notes: Provide more detail/ Highlight result

## Slide 11
Truxton Wash Analysis
Photograph Provided by: Google Maps
Photograph Provided By: AutoCAD Contour map of Truxton Wash
LiDAR Survey Data

## Slide 12
Photograph Provided By: AutoCAD STD. Drawing: SD 6.02-1 Reinforced Concrete Box Culverts
Truxton Wash Analysis
Photograph Provided By: AutoCAD Cross Section of Upstream Box Culvert Invert

## Slide 13
USGS Data for Truxton Wash
Photograph Provided By: HEC-RAS Software, Truxton Wash
Information Provided by: USGS
Photograph Provided By: HEC-RAS Software, Truxton Wash
Photograph Provided By: HEC-RAS Software, Truxton Wash

## Slide 14
Truxton Wash Analysis
Photograph Provided By: HEC-RAS Software, Truxton Wash
12

## Slide 15
Truxton Wash Analysis
Photograph Provided By: HEC-RAS Software, Truxton Wash

## Slide 16: Google SketchUp
Google SketchUP, Artist: Breanna Smith

## Slide 17: Design Criteria Roadway
The American Association of State Highway and Transportation Officials, AASHTO
  Lane Width 11ft. (Chap. 5.2.1)
  Shoulder Width 2ft. (Chap. 5.2.2)
  Sidewalk Width 5ft. (Chap. 4.3.3)
  Barrier for Guard 1ft. (Chap. 4.3.4)
  Barrier for Fencing 1ft. (Chap. 4.3.4)
  Curb Width 1ft. (Chap. 4.3.5)
  Total Bridge Width 42ft.
ADOT
  Striping Width 6in. (M-2 (2/3))
  Double Striping Space 4in. (M-2 (2/3))
BNSF
  Fencing 10ft. (DG A-9)
  Guard Rail 5ft. (DG A-11)
Photograph Provided By: AutoCAD Drawing
Photograph: BNSF Guidelines Grade Separation
Notes: Create better drawing to show this data
Advantages:
  Greater durability
  Longer service life
  Can withstand repeated flooding and subsurface water with less deterioration

## Slide 18: Design Criteria Superstructure
The American Association of State Highway and Transportation Officials, AASHTO
  Portland Cement Concrete Slab 8in. (Chap. 4)
  Top Slab 4in. (Section 13.6) (Chap. 4)
  Girder 4ft. (Section 13.9) (Chap. 4)
  Bottom Slab 6in. (Section 13.6) (Chap. 4)
  Total Superstructure Depth 5.5ft.
Abutment
  10ft. x 23.5ft. (ADOT [BGD 9.7.1.1])
  ASTM C 494/C 494M
Retaining Wall
  100ft. x 2.5ft. x 23ft.
  ASTM C 494/C 494M
Photograph Provided By: AutoCAD Drawing

## Slide 19: Fill Dirt
Fill Dirt
  1:1 Slope
  Engineer Soil: 20,559 Tons
  Top Soil
    ADOT Class 2: Cohesionless soil free from deleterious substances
  Bottom Soil
    ADOT Class 4: Engineered soil
Erosion Control
  Hydroseeding
  Groundcover Plants (English Ivy)
Photograph Provided By : AutoCAD Drawing
Photograph Provided By: Google SketchUp
Notes: Groundcover plants prevent surface erosion. English ivy is a good example of how many plants installed into the slope will bind the surface tightly and cover it all with dense foliage.
Hydroseeding is a method of sowing seed on a large scale for immediate coverage. It is often required at the completion of a project to provide soil holding capacity until other plants mature.

## Slide 20: Type of Concrete
Class S concrete
  Contains Sulfate
  Used for construction of deck and abutments
  As high range water reducing admixture (Superplasticizer): ASTM C 494/C 494M
  Used for cast in place concrete structures
Grade 60 reinforcing steel
  Used for concrete structures
  Recommended by ADOT
Photograph Provided By: northlandconstruction.com
Notes: Discuss in more detail about class S concrete and why it was used

## Slide 21
BNSF Constraints for Construction
Vertical Construction Clearance
Horizontal Construction Clearance
All false work must comply with the above
Chain link fencing
Permanent design clearance Vertical & Horizontal
Limited work to be permitted in the right of way for BNSF
Photograph Provided By: http://media.cleveland.com/
Notes: Vertical Construction Clearances 21 feet above the top of the high rails
Horizontal Construction Clearances, 15 feet measured perpendicular from center line Chain link fence must have openings of 2in. Minimum
The permanent vertical clearance 23’-4”
The permanent horizontal clearance 18’-0”

## Slide 22: Construction of Overpass
As part of the design, Flag-Tech was asked to create a plan for the construction of the overpass
Major Issues:
Leaving the existing road open
Constructing around the railroad without interfering with normal train activities
Photograph Provided By: AutoCAD
Notes: Needs to be placed on sketch up to be more clear

## Slide 23: Construction of Overpass Cont..
To begin the abutments must be placed
The retaining walls will then be added to the east and west side of each abutment
Photograph Provided By: Google SketchUp

## Slide 24: Construction of Overpass Cont…
Addition of the superstructure & deck
Pre-constructed
Photograph Provided By: Google SketchUp
Photograph Provided By: Google SketchUp

## Slide 25: Construction of Overpass Cont…
During Construction of abutments & superstructure
Double box culvert will be constructed
Photograph Provided By: Google SketchUp
Photograph Provided By: Google SketchUp

## Slide 26: Construction of Overpass Cont…
After construction of double box culvert & abutments with deck
Soil 4 and then Soil 2 to be laid out
Diamond Creek Road
Photograph Provided By: Google SketchUp
Photograph Provided By: Google SketchUp

## Slide 27: Construction of Overpass Cont…
After the soil has been properly placed the asphalt and pavement will begin to be added
The lining along with the fencing of the overpass will also be added
Lastly any lining and guardrails will be put together
Photograph Provided By: Google SketchUp
Photograph Provided By: Google SketchUp

## Slide 28: Construction of Overpass Cont…
In conclusion of the construction, the wall positioned previously will be demolished
The soils 4 and 2 will be appropriately added
The overpass is expected to allow traffic flow during this final phase of construction
Photograph Provided By: Google SketchUp
Photograph Provided By: Google SketchUp

## Slide 29: Cost of Staffing
Table 1.1: Cost of Staffing
Notes: Breanna

## Slide 30: Staffing Hours
Table 2.1: Task Hours
Table 2.2: Personnel Hours

## Slide 31: Cost of Engineering Services
Table 3.1: Total Cost of Engineering Services and Expenses

## Slide 32: Cost of Materials

## Slide 33: Special Thanks
Julie Alpert- Transportation Planner Hualapai Tribe, Public Services Department
Kevin Davidson- Hualapai Tribe Planning & Economic Development Director
Philip Wisely PE- Public Services Director
John Tingerthal, MSCE, EdD, PE
Wilbert Odem, PhD PE
Charles Schlinger, PhD, PE, PG
Ian F. Braun, E.I.T., L.S.I.T.
Adam Miele, P.E., Project Manager, City of Flagstaff
Donna Curry, Engineering Specialist, City of Flagstaff
Sayeed M. Hani, Utility Engineering Coordinator/ Railroad Liaison, ADOT

## Slide 34: Questions?
Photograph Provided by: http://supercycle.org.au/quiz-venue-change/
Notes: All