## Slide 1: SAE AERO
Chase Beatty (Team Leader)
Brian Martinez (Organizer)
Mohammed Ramadan (Financial Officer)
Noe Caro (Historian)
Chase Beatty

## Slide 2: CUSTOMER description
Dr. John Tester
  SAE advisor since 2000
Judges at AERO competition
Academic advisor
  Dr. Tom Acker
Chase Beatty

## Slide 3: Project description
Design and build an airplane
Combined dimensions cannot exceed 225”
Take off within 200ft
Land and stop within 400ft
Payload and airplane cannot exceed 55lbs
Fly in a circle at least once
No lighter than air aircrafts or helicopters
Land Land within 400’ 0’
Takeoff within 200’
Brian Martinez

## Slide 4: Project description cont.
Propeller cannot be made out of metal
Fiber-Reinforced Plastic is prohibited
No fuel pump
Cannot used gear boxes—gear ratio
Fuel supplied by competition
No gyroscope
Must raise our own funds
Brian Martinez

## Slide 5: Project schedule
Phase 1: Research
  09/19/11 – 03/01/12
  Equations, materials and airplane design
Phase 2: Fundraising
  09/19/11 – 12/27/11
  Wing-a-thon
Phase 3: Design the Prototype
  10/17/11 – 12/18/11
  Solidworks model
Brian Martinez

## Slide 6: Project schedule cont.
Phase 4: Construction of Final Aircraft
  12/28/11 – 02/15/12
  Wing
  Fuselage
  Landing Gear
Phase 5: Testing the Aircraft
  02/16/12 – 03/07/12
  Performance analysis
Phase 6: Competition
  03/16/11 – 03/18/11
Brian Martinez

## Slide 7: budget
 | Estimated Budget (dollars)
Registration | 600
Fuel Cost (Transportation) | 450
Hotel Cost (4 nights) | 300
Food/Drink Cost | 600
Balsa Wood | 30
Bass Wood | 20
Monokote | 30
O.S. 61FX | 150
Servos | 50
Receiver | 100
TOTAL | 2330
Brian Martinez

## Slide 8: Man power
Time Frame | Hours per week per person | Total hours per person
Fall (9/19-12/16) | 8 | 104
Winter (12/19-1/13) | 35 | 140
Spring (1/16-3/15) | 20 | 180
Total Project Length |  | 424
Chase Beatty

## Slide 9: Fuselage Design 1
Balsa wood shell
Balsa wood ribs inside
Easy wing mounting
Easy tail mounting
Angled tail end
Chase Beatty

## Slide 10: Fuselage design 2
Monokote wrapped around ribs
Hard to mount wings
Lighter weight than Balsa shell
Weaker fuselage
Angled tail end
Chase Beatty

## Slide 11: Fuselage design 3
Combination of first two designs
Solid balsa shell for easy wing mount
Monokote for tail end for lighter weight
Angled tail end
Chase Beatty

## Slide 12: Aerodynamics analysis Airfoil research
Research
Previous teams selection
2010 – E 423
2009 – E 423
Common airfoil
E 423
Clark Y
Our selection for aerodynamics analysis and comparsion
E 423
Clark Y
Mohammed Ramadan
Notes: We should change this slide. This looks like all we’re doing is copying designs from previous years.

## Slide 13: Airfoil Key Parameters
  CL – Lift Coefficient , Cd – Drag Coefficient , Stall , α – Angle of Attack (AoA)
  Lift to Drag Ratio
Mohammed Ramadan
Stall: is a sudden drop in the lift coefficient when reaching a critical AoA

## Slide 14: Airfoil Analysis
(Lift Coefficient vs AoA)
Mohammed Ramadan
Profili
E 423
Max Cl = 1.89 at 12
Stall beginning at12
Clark Y
Max Cl = 1.39 at 12
Stall around 12 to 15

## Slide 15: Airfoil Analysis CONT.
Mohammed Ramadan
(Drag Coefficient vs AoA)
E 423
Cd= 0.035 at 12
Cd = 0.02 at 9
Clark Y
Cd= 0.030 at 12
Cd = 0.015 at 9
Profili

## Slide 16: Airfoil Analysis CONT.
(Lift to Drag Ratio vs AoA)
Mohammed Ramadan
Profili
E 423
L/D max = 97 at 6°
Clark Y
L/D max = 79 at 6°
Maximum L/D is an
important parameter
in airfoil performance
efficiency

## Slide 17: Airfoil Design
Mohammed Ramadan
SolidWorks & Profili
4 lightening holes
3 spar locations
Initial chord = 13 inches
Max thickness = 1.63 inches

## Slide 18: Wing Planform
Rectangular
Ideal for low speed
Ease to construct
Tapered
Harder to construct
Good for high speed
Mohammed Ramadan

## Slide 19: Wing Dimension
Initial Dimensions
Wing span = inches
Wing chord = inches
Area = span X chord =
Aspect ratio = = 6.9
AR for low speed = 6 or greater (John D. Anderson, Jr.)
, ,
Mohammed Ramadan
Wing calculation

## Slide 20: Wing analysis
Static analysis for load distributions
Mechanics of materials for yield strength.
Mohammed Ramadan

## Slide 21: Landing gear
Tail dragger or Tricycle
COG
Takeoff
Landing
Brian Martinez

## Slide 22: Takeoff and landing calculations
= Takeoff Velocity
= Stall Velocity
= Landing Distance
= Touchdown Velocity
W = Weight
  ρ = Air Density
  A = Constant
  B = Constant
)
Brian Martinez

## Slide 23: engine
OS .61 FX
Required for regular class at SAE competition
19.4 oz
2,000 – 17,000 RPM
1.90 HP @ 16,000 RPM
Research for equations involving the engine still in progress
Brian Martinez

## Slide 24: Tail End selection
We did research on three different tail sections
  Convectional
  T-Tail
  Cruciform
We will use a Convectional tail with a NACA-0012 airfoil
  Easy to manufacture
  Vertical tail will have a taper
  NACA airfoil is popular and should provide necessary stability
(Raymer)
Noe Caro

## Slide 25: Horizontal Tail section
An Aspect Ratio of 4 will be used for the horizontal tail section
  This horizontal span will be about 29 in with a chord of 7.5 in
There will be no taper in the horizontal tail
Equations:
Planform Area
Horizontal Span
Horizontal Chord
(Anderson)
Noe Caro

## Slide 26: Vertical tail section
Aspect Ratio will be 1.5
The vertical tail will be tapered at a ratio of 50%
Will have a root chord of 7.5 in
Will have a tip chord of 4 in
Will have a span of 11.5 in
Equations:
Planform Area
Vertical height on tail section
Root chord
Tip chord
Noe Caro

## Slide 27: Conclusion
Calculate equations related to the airfoil, fuselage, tail wing and engine
Put together final solid works model
Put together a materials list
Order materials needed to construct prototype
Noe Caro