## Slide 1: NAU AERO TEAM 2012
The Lumberjacks
Team 017
03/16/12
Brian Martinez

## Slide 2: AERO TEAM
Capstone Members
  Chase Beatty
  Mohammed Ramadan
  Noe Caro
  Brian Martinez
SAE Advisor
  Dr. John Tester
Academic Advisor
  Dr. Tom Acker
Brian Martinez

## Slide 3: DESIGN OVERVIEW
Components
  Wing Design
    Airfoil (E 423)
    Non-tapered
  Fuselage
  Landing Gear
  Tail
    Airfoil (N-14)
Brian Martinez
Notes: Airplane consists of a under-campered. We researched flat bottomed, over-campered.

## Slide 4: PROJECT SCHEDULE
October 1st –December 15th – Research, Trade Studies
December 15th-January 6th –Solid works modeling
January 1st-February 1st- SAE Report writing
February 1st-February 24th-Construction of plane
February 25th –flight test
Went over construction of plane, which cancelled our flight test.
Construction wasn’t done until March 10th
Brian Martinez

## Slide 5: MATERIALS
Balsa Wood
  Majority of the airplane
Bass Wood
Honeycomb (Aluminum)
Engine
  OS .61 FX
Monokote
Brian Martinez

## Slide 6: FINAL DESIGN
Brian Martinez

## Slide 7: TAIL SIZING
Noe Caro
Horizontal Tail
An Aspect Ratio of 4 will be used for the horizontal tail section
  This horizontal span will be about 32 in with a chord of 9 in
There will be no taper in the horizontal tail
(Anderson)
Vertical Tail
Aspect Ratio will be 1.5
The vertical tail will be tapered at a ratio of 50%
Will have a root chord of 11.75 in
Will have a tip chord of 4.5 in
Will have a span of 14 in

## Slide 8: CENTER OF GRAVITY
Noe Caro
C.G. is located 15.61 inches without payload from the tip of engine
C.G. is located 15.03 inches with payload from the tip of the engine

## Slide 9: STABILITY & CONTROL
With C.G. we found the static margin using Aerodynamics, Aeronautics, and Flight Dynamics, John Wiley
Found that the plane was stable with and without payload
Neutral points were 2.18 and 2.74 inches from C.G.
Noe Caro
Using different speeds
Based on results used different servos for elevator than the rudder and ailerons.
(Referenced from Aircraft Proving Ground)

## Slide 10: PROPULSION TESTING
Testing done with different propellers at elevation similar to Van Nuys.
Results indicated should use a 14*4 propeller

## Slide 11: WING DESIGN
Mohammed Ramadan
Wing span = 84 inches
Chord = 13 inches
Aspect Ratio =6.5
Rectangular Planform
Four lightening holes on
the airfoils
Three spar locations
Wing is built completely from
balsa wood

## Slide 12: PERFORMANCE (DRAG & LIFT)
Mohammed Ramadan
The calculated total Drag of the aircraft from induced drag, lift drag, and cooling drag
is 0.126

## Slide 13: PERFORMANCE (TAKEOFF)
Chase Beatty
Chart: Take-off Distance
| 19 | 20 | 21 | 22 | 23 | 24
 | 154.97 | 163.25 | 171.8 | 180.65 | 189.79 | 199.2

## Slide 14: Wing Structural Analysis
22 lb loading with ends of the wings fixed
Maximum Stress- 2600 psi
Maximum displacement- 1.1 in
Yield Stress of balsa- 3000 psi
Chase Beatty

## Slide 15: CONCLUSION
4 main categories
  Wing Design
  Stress Analysis
  Center of Gravity
  Performance

## Slide 16: QUESTIONS?
Chase Beatty

## Slide 17: REFRENCES
Anderson, John D., fundamentals of Aerodynamics, McGraw-Hill, New York, 2011
B. W. McCormick, Aerodynamics, Aeronautics, and Flight Dynamics, John
Wiley, 1995
Garner, W. B., “Model Airplane Propellers” 2009
Nicolai, Leland M., Estimating R/C Model Aerodynamics and Performance, Lockheed Martin, 2009
Aircraft Proving Ground. -http://www.geistware.com/rcmodeling/calculators.htm
Raymer, Daniel P., Aircraft Design: A Conceptual Approach, American Institute of Aeronautics and Astronautics, Virginia, 1999
Philpot, Timothy. Mechanics Of Materials. Hoboken: John Wiley and Sons Inc, 2008. 411-421.
Anderson, John D., aircraft performance and design, McGraw-Hill, New York, 1999