## Slide 1: Alternative Power Source for Dental Hygiene Device
Team 15:
Nizar Almansouri
Ningbiao Jiang
Francisco Heath
Jin Niu
Jiaqi Xie
Engineering Analysis

## Slide 2: Contents of Presentation
Problem Statement
Design Overview
Battery Specifications
Inverter Selection
Packaging
Charge Indicator
Gantt Chart
References
1

## Slide 3: Problem Statement
NAU Department of Dental Hygiene
Humanitarian work in remote areas
No electricity available to power Wig-L-Bug

## Slide 4: Design Overview
Battery
Inverter
Wig-L-Bug

## Slide 5
FAA Regulations
Equivalent Lithium Content (ELC). ELC is a measure by which lithium ion batteries are classified.
8 grams of equivalent lithium content are equal to about 100 watt-hours.
25 grams of equivalent lithium content are equal to about 300 watt-hours.
Passengers can carry Up to 2 spare lithium ion batteries, not installed in a device (between 8 and 25 grams aggregate)

## Slide 6: Battery Specifications
Capacity | 250Wh
Nominal Voltage | 12.6V
Max Discharge Rate | 10 A
Dimensions | 5 x 4 x 2 in
Weight | 2.4 lb
Grams equivalent lithium | ~ 20 g
Two batteries will provide enough power to run the device all day
Batteries will be separate to meet FAA regulations

## Slide 7: Inverter Analysis
Specification | Pure sine wave inverter | Modified sine wave inverter
Input Voltage | 10~15V DC | 10~15V DC
Output Waveform | Pure Sine Wave | Modified Sine Wave
Output Voltage | 120V AC at 60Hz | 120V AC at 60Hz
Maximum Power | 250W | 210W
Continuous Power | 150W | 150W
Maximum Efficiency | 90% | 90%
THD | <3% | <40%
Size | 7.25×5×2.25in | 5×3.25×1.8in
Weight | 2lb | 1.5lb
Cost | $65 | $25

## Slide 8: Inverter Analysis
Output Waveform
Pure sine wave and modified sine wave

## Slide 9: Inverter Analysis
Harmonic Distortion
Harmonic distortion of the electrical current waveform

## Slide 10: Inverter Analysis
Total Harmonic Distortion (THD)
THD =
Pure sine wave inverters are more expensive, but will run all AC loads, and are best for sensitive electronics.

## Slide 11: Charge Indicator
A small set of LEDs that indicates state of charge
Possible addition if time allows

## Slide 12: Packaging
Resists rough handling
Complies with FAA regulations
Cheap and Lightweight

## Slide 13: Gantt Chart

## Slide 14: Conclusion
Battery only Design
Battery Specifications
Inverter Analysis
Charge Indicator
Packaging
Total Cost | $350
Total weight | 9lb
Packaged Size | 8 x 5 x 7 in
Energy Capacity | 500 Wh

## Slide 15: References
http://www.bomara.com/powerware/wp_harmonics.htm
http://www.stecasolar.com/index.php?Inverter_selection
http://www.ebay.com/itm/DC-12V-5A-Lithium-battery-pack-20000-Mah-capacity-2A-charger-for-CCTV-camera-/150900422397?pt=US_Rechargeable_Batteries&hash=item23225db6fd
http://safetravel.dot.gov/

## Slide 16: Questions ?