## Slide 1: Helium Micro Air Vehicle
Fawaz Alenezi, Hamoud Alkhaldi, Abdulrahman Almuqhawi, Matthew Kohr, Conrad Nazario and Randal Spencer
Department of Mechanical Engineering
April 29, 2016

## Slide 2: Overview
Introduction
Project Needs and Goals
Objective
Helium Blimp
  Steering System
  Power Source
  Enclosure Designs
  Camera Connections and Setup
  Electronic Setup
Testing and Results
Bill of Materials
Conclusion

## Slide 3: Introduction
Dr. Srinivas Kosaraju, our client, is a lecturer in the department of Mechanical Engineeering at Northern Arizona University
Dr. Kosaraju has requested to design and test a Helium Micro Air Vehicle (MAV) device to fly over fires and contaminated areas
The MAV will be designed to carry electronics and collect pictures while in flight

## Slide 4: Project Needs and Goals
Need
  Conventional micro air vehicles are not suitable for long duration flight for surveying
Goals
  Develop a Micro Air Vehicle (MAV) that can ascend, descend, and survey areas more efficiently while using helium as its main source of lift
  Limit energy consumption during flight so that the MAV’s power source will last longer than commercial MAVs

## Slide 5: Objectives
Objective | Measurement | Units
Reduce Weight | Mass | kg
Optimize Flight Time | Time | sec
Minimize Cost | Currency | $
Maximize Thrust | Force | N
Easy to Store | Volume | m3

## Slide 6: Constraints
Reach a minimum height of 30.5 m (100 ft)
Must have mounted camera
Remote controlled guidance system
Must move forward, ascend, descend and hover at a specified altitude
$2000 budget

## Slide 7: Helium vs Hydrogen
Advantages
  Inert gas/nonflammable
Disadvantages
  More expensive than hydrogen
  Weighs twice as much as hydrogen
    Hydrogen can lift about 8-11% more
Source: smithsonianmag.com
Source: © Disney. All rights reserved

## Slide 8
State of the Art Research
Airlander 10
Air Penguin
Volume: 38,000 m3
Kevlar, Mylar, and Vectran
Payload capacity: 10,000 kg
Flight duration: 5 days
Length: 3.70 m
Aluminium-Metallised Foil
Li-Po battery, 2000 mAh, 4.2 V
Ultrasound Receiver Capsules
Source: .hybridairvehicles.com
Source: festo.com

## Slide 9: Final Design

## Slide 10: Final Design
Propellers
Motors
L-Bracket
Servo
Carbon Fiber Rods
Spacers
Electric Box
Flange
PVC Shaft
Enclosure
Bolts

## Slide 11: Blimp Testing Procedure
Filled the blimp with Helium gas
Used an entire tank of Helium ~ 6.14 m3
Attached testing enclosure to the bottom of the blimp
Added weights in increments to measure maximum carrying capacity
Measured dimensions of the blimp

## Slide 12: Helium Blimp
Length: 4.88 m
Center Blimp Diameter: 1.91 m
Carrying Capacity: 3.11 kg

## Slide 13: Propellers
Diameter: 30 in.
Pitch: 5.5 in.
High thrust is needed to counter the Helium lift force
Propeller selection was based on two parameters:
  Large diameter
  Small pitch
Dynam Carbon Fiber Propellers
Source: hobbyking.com

## Slide 14: Motors
Motor with a low KV provides optimal thrust
Using LDPOWER M4114-320KV Brushless Motor (CW)
  999W
  320KV
  14.8V-22.2V (4S-6S)
Battery with 6 cells (6S), each cell 3.7V, has been chosen to maximize the thrust
Source: hobbyking.com

## Slide 15: Power Source
Turnigy nano-tech 2000mAh 2S(7.4V)1P 20~40C to power the servos
  Weight: 0.098 kg
MultiStar LiHV High Capacity 6S(22.8V) 5200mAh Multi-Rotor to power the motors and electronic speed controllers
  Weight: 0.613 kg
  Thrust: 10.5 N
Source: hobbyking.com
Source: hobbyking.com

## Slide 16: Servos
Servo
  Turnigy™ TGY-5521MDHV
  Light Servo at weight of: 0.0635 kg
  Torque at 22kg/cm
  Operates at a maximum of 8.4 V
Source: hobbyking.com

## Slide 17: Enclosure Design
The enclosure is made of polycarbonate
Velcro attached to the top
Bolt in each corner to adjust height

## Slide 18: Initial Frame Design
The shaft design is made of PVC
Final weight: 3.2 kg
Exceeds maximum carrying capacity

## Slide 19: Frame Design Modifications
PVC shafts, replaced with carbon fiber hollow shafts
The PVC Tee fitting, replaced with a plastic electric box
L brackets were added to support the motors
L bracket attached to the plastic casing where the camera will be mounted
Springs attached to L brackets to minimize strain on the servos’ motor
Source: homedepot.com
Source: easton.com

## Slide 20: Final Frame Design
Ribbons used to reinforce bottom Deflection
Wiring wrapped along shafts

## Slide 21: Camera Setup
Lynx 1080p
Raspberry pi 2
64 GB Micro USB
Delay and range functions
Skip function
Automatic Startup when power is applied

## Slide 22: Quadrino and Radio Transmitters
Flight Controller
In flight communication
GPS
Telemetry data
Source: Lynxmotion
Source: Lynxmotion

## Slide 23: Quadrino Interface

## Slide 24: Receiver
Spektrum AR610 channel receiver
Communicates with Spektrum DX6i Transmitter
Powered by the Quadrino
Source: hobbyking.com

## Slide 25: Electronic Speed Controller (ESC)
Connection point between battery and signal output for motors
ESC will directly connect to receiver
Going with the ZTW Spider 40 amp
Servo split cable
Connects to throttle channel
Source: amazon.com

## Slide 26: Electronic Setup
Rocker Switch
  Able to turn off and on power supply
  Centralized power supply
  Outputs to servos and motors
Quadrino operates by a separate 5V battery

## Slide 27: Power Schematic

## Slide 28: Final System

## Slide 29: Thrust Testing Setup
Determining thrust force
Equipment used
  Long wood board
  Cargo Scale
  Ribbons
  Clamps
  Velcro

## Slide 30: Thrust Calculations

## Slide 31: Results
Blimp carrying capacity: 3.11 kg
The system weight: 2.85 kg
Force Required (3.11-2.85)kg= 0.26 kg = 2.55N
Force generated: 0.45 kg = 4.41N

## Slide 32: Flight Testing

## Slide 33: Mounted Camera Footage

## Slide 34: Bill of Materials
Name | Cost ($) | Weight (kg)
Surveillance System | 126.03 | 0.122
Blimp/ Maintenance | 751 | NA
Propulsion System | 285.56 | 1.217
Attachments | 19.98 | 0.062
Enclosure System | 16.97 | 0.733
Telecommunication System | 441.22 | 0.171
Steering System | 70.43 | 0.220
Total | 1811.19 | 2.85

## Slide 35: Conclusion
The client requested to design and test the Helium MAV
The final design performed as designed, with no testing flaws from the enclosure
Team obtained camera footage from the test flight
Final design came under weight of the payload capacity, with approximately .26kg of excess lift capacity
The net force obtained after testing was 1.86N of extra thrust capability

## Slide 36: Acknowledgments
NAU Machine Shop
  Tom Cothrun
  Zach Goettle
  Perry Wood
  Zach Rischar
Peers
  William Richie
Professors
  Dr. Srinivas Kosaraju

## Slide 37: References
[1] "Nano-Tech 2.0," Turnigy, 2016. [Online]. Available: http://www.hobbyking.com. [Accessed 1 April 2016].
[2] Carlon, 15 January 2016. [Online]. Available: http://www.homedepot.com/. [Accessed 2016].
[3] Lynx Motion, 26 January 2016. [Online]. Available: http://www.lynxmotion.com/. [Accessed 2016].
[4] "Spider Multirotor ESC," ZTW, January 2016. [Online]. Available: http://www.buddyrc.com. [Accessed 28 March 2016].
[5] "Physical Computing," Python, 2016. [Online]. Available: https://www.raspberrypi.org/. [Accessed April 11 March 2016].
[6] "6 channel Receiver," Flysky, January 2016. [Online]. Available: http://www.hobbypartz.com/. [Accessed 2016].
[7] H. M. Capstone, Interviewee, Dr. Srinivas Kosaraju. [Interview]. 18 April 2016.
[8] "Transmitter and Reciever," Exceed RC, [Online]. Available: http://www.hobbypartz.com. [Accessed April 2016].
[9] "Turnigy TGY-20c, Turnigy Battery Pack," 13 February 2016. [Online]. Available: http://www.hobbyking.com/. [Accessed 28 May 2016].
[10] H. A. A. A. M. K. C. N. R. S. Fawaz Alenezi, "Helium Micro Air Vehicle," NAU, [Online]. Available: http://www.cefns.nau.edu/capstone/d4p/.
[11] "Voltage ESC," RoHS, 2016. [Online]. Available: www.amazon.com. [Accessed April 2016].
[12] "Hindenberg Disaster," Smithsonian, [Online]. Available: www.smithsonianmag.com. [Accessed April 2016].

## Slide 38: Questions?