## Slide 1: Sumo Team A Team 8
Robotics Competition
Hunter Lane, Graham Rose, Sean Sussman, Jordan Ziegler
April 28th, 2017

## Slide 2: Project Description
Head-to-head match following traditional human sumo matches
  Pushing match only; no weapons, no flipping, no jamming, no projectiles, no liquids
Three design tasks
  Remote controlled mega sumo
  Autonomous mega sumo
  Additional showcase design
Showcase design chosen was
a 10-pound combat shell
4/28/17, Jordan Ziegler, Slide 2

## Slide 3: Project Requirements
Requirements are limited, creativity is highly encouraged
Sumo Specifications
Autonomous control must be fully contained, receive no external signals
RC motion directly due to teleoperation of the operator
Combat Specifications
No size requirements
Tethered projectiles only, no liquids, no damaging the arena
School Restrictions – No projectiles, no flames
4/28/17, Jordan Ziegler, Slide 3

## Slide 4: Project Requirements – Engineering Requirements
Customer Needs generated using official competition rules
Engineering Requirements generated using Customer Needs
Same requirements for all competitions
4/28/17, Sean Sussman, Slide 4

## Slide 5: Design Solution - Overview
Final Design includes two Designs
A single sumo robot capable of remote and autonomous control
A wedge-style combat shell, using same internal components as sumo
4/28/17, Sean Sussman, Slide 5

## Slide 6: Design Solution – Mechanical Components
High speed, high torque Maxon Motors: 15V, 7180-rpm, 73.1-mNm of Torque
Two wheel design: 65 shore A hardness to maximize friction, minimize impact shock
4/28/17, Hunter Lane, Slide 6

## Slide 7: Design Solution – Mechanical Components
Hardened steel gears: 3-stage 6,4:1 reduction ratio
6 neodymium magnets to increase downward force
4/28/17, Hunter Lane, Slide 7

## Slide 8: Design Solution – Electrical Components
Sabertooth 2x32 Dual-Speed-Controller
  Supply 15-30V and 32 Amps per channel
  Reads RC & autonomous inputs
Arduino Uno for Autonomous Control
4/28/17, Graham Rose, Slide 8

## Slide 9: Design Solution – Electrical Components
2 Pepperl+Fuchs infrared sensor for opponent detection
4 QTR1A contrast sensors for edge detection
Lithium polymer battery: 30C, 2200mah
4/28/17, Graham Rose, Slide 9

## Slide 10: Manufacturing – Sumo Frame
Frame constructed with 1/8th-inch mild steel, 28-gauge galvanized steel plates
  Frame pieces attached with tack welds
  steel plates are attached with JB weld
Electronics held in 3D-printed housing
Gears used as a 2-stage reduction
  Mounted on 1/4th-inch stainless steel rods
4/28/17, Hunter Lane, Slide 10

## Slide 11: Manufacturing – Combat Shell
Frame constructed with 1/4th-inch aluminum
3D-printed internal components for electronics mounting
4/28/17, Sean Sussman, Slide 11

## Slide 12: Manufacturing – Electronical Circuit
4/28/17, Graham Rose, Slide 12
Edge
Sensors
Opponent
Sensors
Motors
Battery
Microcontroller
Speed Controller

## Slide 13: Manufacturing - Programming
Autonomous functionality programmed in the Arduino Sketch Language
Arduino uses Pulse-Width-Modulation (PWM) signals ranging from 0-5Volts to control the motors
4/28/17, Graham Rose, Slide 13

## Slide 14: Testing Proofs
8 tests conducted to ensure final designs met all Engineering requirements
4/28/17, Hunter Lane, Slide 15

## Slide 15: A special thank you to…
Tom Cothrun for his assistance modifying hardware and assistance in shaft/gear mounting
Dr. John Sharber for his assistance in designing the electrical circuit
The NAU Baja Team for their material donations

## Slide 16: Sponsors

## Slide 17: References
[1] “Unified Sumo Robot Rules”, Robotgames.net. 2016, Web. 25 Sept 2016.
[2] Massachusetts Institute of Technology, “Sumo Robots,” MITMECHE. Dec 2014.
[3] motors and drive systems | maxon motor", Maxonmotorusa.com, 2016. [Online]. Available: http://www.maxonmotorusa.com/maxon/view/content/index. [Accessed: 23- Nov- 2016].
[4] F. Dede, "How to Make a Sumo Robot", Jsumo.com, 2016. [Online]. Available: https://jsumo.com/how-to-make-sumo-robot/. [Accessed: 23- Nov- 2016].

## Slide 18: Questions?

## Slide 19: Manufacturing - Programming
4/28/17, Graham Rose, Slide 14