## Slide 1: Collegiate Wind Competition ‘19 – Mechanical Design
Faisal Alrashidi
Naser Alrashidi
Tanner Lehr
Riley Sinek
4/26/19

## Slide 2: Project Description
U.S. Department of Energy is the sponsor
Collegiate Wind Competition
  Competition held in Boulder, Co. May 6th-9th
  Sixth team representing NAU at the Competition
  Collaboration with Electrical Engineers
1 of 12 Universities invited to competition
Faisal 1

## Slide 3: Project Description contd.
Tunnel Turbine
  Cut-in task
  Safety task
  Durability task
  Power curve task
  Rated RPM and power control task
Faisal 2

## Slide 4: Customer Requirements
Single Tail Yaw
Pitching Mechanism
Early Cut-in
Efficient Yawing
Reliable Braking System
Modular Design
Wind Tunnel Volume and Access Limits
Naser 3

## Slide 5: Engineering Requirements
Cut-in between 2.5m/s and 5m/s
Yaw rate up to 180°/s
Reduce rotor speed to 10% of rated rpm within 10s
Must fit through 122cm by 62cm door
Turbine parts must stay with a 45x45x45 cm3 cube
Shaft height must be 60±3cm above base plate
Naser 4

## Slide 6: Design Motivation
Blade | Yaw | Nacelle | Shaft | Brake | Tower
Carbon-fiber reinforced nylon filament | Pyramid-shape and size | 3 Levels Store ME and EE components | Two different diameters Two flat surfaces Attach to Generator | Linear actuator Brake caliper with mountain bike pads Bearing block holder for shaft | 1018 Steel 1.5” OD 1” ID
Naser 5

## Slide 7: Final Design
Final model from SolidWorks
Naser 6

## Slide 8: Final Design - Blades
Blades were designed using Blade Element Momentum theory
  MATLAB was used to optimize the blade geometry
  Increased chord length to achieve high rotor solidity
Riley 7

## Slide 9: Airfoil Selection
Three airfoils were integrated into the blade design
  High cambered airfoils were chosen based on the low Reynold’s Number Regime
Riley 8

## Slide 10: Blade Safety Analysis
FEA for the blade throws a minimum factor of safety of safety of 0.756
  Caused by small stress concentration near blade root
Riley 9

## Slide 11: Final Design - Hub
Integrated a pitching mechanism for turbine
  Six design iterations before beginning machining
  Incorporated Triangular hub and “claws”
  All components were manufactured in-house
Riley 10

## Slide 12: Active Pitching Mechanism
The mechanism was designed to achieve early start-up and avoid stall during operation
Mimicked helicopter mechanism to control attack angle of blades
  Swashplate with two linear actuators to control blade pitch
Riley 11

## Slide 13: Force Analysis on the Hub
FEA showed safe results for confidence in final design:
  Minimum F.S. for Hub: 1.18
  Minimum F.S. for claws: 1.48
Riley 12

## Slide 14: Final Design Shaft
Used two flat surfaces instead of keyway
  Based on the individual analysis this was best
The material is 1018 steel
Manufacturing operations
  Lathe
  Mill
  Tap
Factor of Safety for the design
  2.2
Naser 13

## Slide 15: Final Design Yaw-tail
Maximized surface area
Center of gravity moved back further
3D printed with ABS plastic
  Aluminum was harder to manufacture
  The tail was printed in two pieces and epoxied together
Faisal 14

## Slide 16: Tail-yaw FEA
Effective Drag Force on the tail
  20N
Factor of Safety for the design
  2.2
Faisal 15

## Slide 17: Final Brake Design
Designed brake caliper around a linear actuator
  4 iterations were made
  Incorporated bearing block into caliper
  Brake pads are from a mountain bike
Designed rotor disc brake
  Modeled after small scale RC car disc brakes
All pieces were CNC'd in house
Tanner 16

## Slide 18: Brake Testing
Tested forces using kitchen scale
  Scale was in grams --> converted to Newtons
10 tests showed an average of 21.68N
  Actuator rated for 22N
Tanner 17

## Slide 19: Final Designs Tower & Yaw Bearing
Tower
  1018 Steel
  Easy to machine
  Tensile strength is 370 MPa
Welded base plate
  1018 Steel
Yaw Bearing Assembly
  Two deep grove ball bearings
  Retaining Ring
Tanner 18

## Slide 20: Tower FEA and Yaw Bearing Testing
Yaw Bearings
  Deep Grove Ball Bearings rated for 15,000 rpm
SolidWorks FEA
  Max deflection: 0.126 mm
  Minimum Factor of Safety: 45.58
Tanner 19

## Slide 21: Final Design Nacelle
6061 Aluminum
3 "Levels"
  Top: brakes, shaft, and generator
  Middle: rectifier
  Bottom: slip ring
Slots added so placement of everything can be changed as needed
Tanner 20

## Slide 22: Nacelle FEA
Factor of Safety: 180.2
Max Deflection: 1.72*10-4 mm
Tanner 21

## Slide 23: Budget
Actuators, motors, and Arduino: $1081.96
Building Materials: $207.28
Blade Material: $145.61
Epoxy and Glue: $58.15
Miscellaneous: $114.56
Total: $1753.02
Actuators, Motor, & Arduino
Building Materials
Blade Material
Miscellaneous
Epoxy and Glue
Tanner 22

## Slide 24: Thank you to...
W.L. Gore and Associates
The U.S. Department of Energy
David Willy
Dr. Oman
Amy Swartz
Riley 23

## Slide 25: Questions?