## Slide 1: SunTrac Braze-Welding Jig
Kadeja Alhossaini
Nathan Firor
Edwin Smith
Ethan Vieane
5 April, 2020 - Northern Arizona University

## Slide 2: Project Introduction: Client
Suntrac USA is a hybrid climate systems company
  Based in Tempe, AZ
  Manufacture a solar energy heat exchanger to be used in AC and HVAC systems
  Save 40% on cooling energy costs with a panel hooked up to an HVAC unit
Projected to grow company to meet increase in product demand
  Require new practices to increase production efficiency
  Decrease idle workspace
Vieane 1

## Slide 3: Project Introduction: Task
Design, Build, and Test a braze welding jig that is compatible with SunTrac’s 4ft, 6ft, and 8ft products
  Provide a completed CAD package with assembly drawings
  Create part list, BOM, and final cost estimate
  Build a full scale prototype
  Test prototype for engineering requirements
  Create an Operation and Assembly Manual
Figure 2: Current 8 Foot Manifold Jig
Vieane 2

## Slide 4: Requirements and Specifications
The Customer Requirements (CRs) were developed after speaking with the client at SunTrac. Each customer requirement has at least one Engineering Requirement (ER) set to it.
Table 1: Customer Requirements & Engineering Requirements
Vieane 3

## Slide 5: Conceptual Design
Sub-Assembly
Jig Face
  Telescoping Tubes
  Power Screw
  End Plate
Jig Frame
  Locking Assembly
  Guide Rail
  Wire Rope
  Pulley
  Winch
Smith 4
Figure 3: Final Prototype

## Slide 6: Manufacturing Design: Details
Visit the client’s manufacturing facility for 3 consecutive weekends
  Week 1: Jig face 2x2’s and Jig Frame 2x4’s cut to size, pin holes drilled
  Week 2: Bolt and weld all subassembly connections for a finalized Jig Frame
  Week 3: Attach end plates to telescoping tubes, weld Jig Face to Frame
Convene as a group on design revisions
  Involve client in final consensus on debatable revisions
Smith 5

## Slide 7: Manufacturing Design: Documentation
Figure 4: Jig Face
(4 Foot Configuration)
Figure 5: Front View of Jig Frame
Figure 6: Side View of Jig Frame
Smith 6

## Slide 8: Manufacturing Design: Computational Analyses
Smith 7
Guide Rail Structural Analysis
  Expected center deflection of 0.26’'
  Negligible rotation
  Justifies adding an extra support
Figure 8: Locking Assembly FEA Analysis
Figure 7: Guide Rail Structural Analysis
Locking Assembly FEA Analysis
  Stress concentration at back side carriage connection
  High eye bolt stresses for tear-out
  Factor of safety of 2
  No support needed

## Slide 9: Testing
The testing procedures implemented were set to satisfy each Engineering Requirement.
Most of the tests were designed to validate multiple ER’s
Predetermined Design Validation
Manufacturing Contingencies
Complete Prototype Testing
Table 2: Testing Procedures & Engineering Requirements
Firor 8

## Slide 10: Final Product: Gallery
Figure 9: Winch and Mount Augment
Figure 11: Jig Frame With Winch and Locking Mechanism
Figure 10: Back View of Pulley
Figure 12 : Locking Mechanism Close Up
Firor 9

## Slide 11: Final Product: CAD Comparison
The prototype was built with the all of the mechanical components utilized in the CAD model and detailed in the BOM.
Firor 10
Figure 13: CAD of Mechanical Components
Figure 14: CAD Reflected Jig Features

## Slide 12: Budget
The budget for this project is $1600.00 as set by SunTrac
  Total Price at $1413.13
Subassembly prices are listed in the right column of figure 15
Full Bill of Materials (BOM) found in Appendix A.1
Figure 15: Sub-Assembly Price Breakdown
Alhossaini 11

## Slide 13: Future Work
Alhossaini 12
5
Final Website
To document the teams progress and final product.
4
Final Report
To account for all the changes on the design to achieve the final product.
3
Final Tests on the Device
SunTrac invited the team back to finish tests over Summer 2020
Operation & Assembly Manual
To ensure the manufacturing and assembly process is followed.
2
1
Final Welds to Combine Sub-assemblies
SunTrac wants to suspend visits till further notice due to COVID-19 outbreak.

## Slide 14: Thank You For Listening
For any questions please email the team:
Kadeja Alhossaini: ka956@nau.edu
Nathan Firor: naf76@nau.edu
Edwin Smith: ejs328@nau.edu
Ethan Vieane: esv25@nau.edu
Alhossaini 13
Figure 16: Team Selfie in SunTrac

## Slide 15: References
[1] https://www.suntracusa.com/gallery

## Slide 16: Appendix A.1 - Bill Of Materials
Table 3: Bill of Materials