## Slide 1
Hopi 50 MW Solar PV Power Plant
Hopi Solar Capstone Team, Northern Arizona University, Flagstaff, AZ 86011
Mohammed Alajmy, Marlon Cortez, Jordan Masayesva, Kaarina Nehring
The team is committed to researching and advising the Hopi Tribe towards a solution for their lack of power independence and job availability. Our team made a feasibility study for a hypothetical 50-megawatt solar power plant that will produce Hopi-owned energy and provide a reliable job source. This project involved working with Hopi representatives and the National Renewable Energy Laboratory (NREL) to produce a hypothetical solution for solar power generation on Hopi land. During this project, the team has performed the following tasks:
1. Solar resource assessment based on a Typical Meteorological Year (TMY).
2. A site selection process
3. Energy conversion system sizing, design, and analysis of the PV Power Plant, including: PV Module Selection, Inverter Selection, Racking/Tracking System Selection, Overall System Design, Grid/transmission considerations, System degradation calculations, and Annual Energy Production (AEP) calculations
4. Financial modelling including, but not limited to: Life Cycle Cost analysis, Levelized Cost of Energy (LCOE), Other Financial modelling as needed and revenue, incentives, and depreciation calculations, Identification of the entity to hypothetically sell the electricity to , Perform Power Purchase Agreement (PPA) calculations, and Energy policy considerations.
5. Hopi Tribe’s cultural and political considerations
Abstract
Data
Results
Conclusion
As the design sits currently, we are satisfied with the results. The power plant has an overall efficiency of 86% with our inverter and module choices. The team has recently been introduced to a company who design, installs and maintains a variety of power generation facilities in the United States. The team plans to get further insight into what truly goes into designing and installing a solar power plant of this size. From this professional advice we may be able to iterate on our current design and include costs and constraints that we have not foreseen.
References
[1]"Photovoltaics (PV) Systems", Nfpa.org, 2020. [Online]. Available: https://www.nfpa.org/News-and-Research/Resources/Emergency-Responders/High-risk-hazards/Photovoltaics-Systems. [Accessed: 04- Aug- 2020].
[2] Canadian Solar, Canadiansolar.com, 2020. [Online]. Available: https://www.canadiansolar.com/wp-content/uploads/2019/12/Canadian_Solar-Datasheet-HiKu_CS3L-P_EN.pdf. [Accessed: 19- Jul- 2020].
[3] “Canadian Solar 400W PV Module 144 ½ Cells CS3W-400PB-AG - A1 Solar Store,” A1SolarStore. [Online]. Available: https://a1solarstore.com/canadian-solar-400w-pv-module-144-cells-cs3w-400pb-ag.html?gclid=EAIaIQobChMIzvSd0YeC6wIVycDACh1N5wYSEAQYASABEgIYgPD_BwE. [Accessed: 04-Aug-2020].
[4] “10 AWG Solar Photovoltaic Wire 600V UL 4703 (PV Wire),” Wire and Cable Your Way. [Online]. Available: https://www.wireandcableyourway.com/10-awg-solar-pv-photvoltaic-ul4703-wire.html?gclid=EAIaIQobChMImMmlyIuC6wIVS73ACh0mNgZmEAQYASABEgKqbPD_BwE. [Accessed: 04-Aug-2020].
[5] “2-2-2-4 Dyke Underground Secondary Distribution Cable,” Wire and Cable Your Way. [Online]. Available: https://www.wireandcableyourway.com/2-2-2-4-dyke-underground-secondary-distribution-cable.html?utm_source=google-shopping&utm_medium=organic&gclid=EAIaIQobChMI9tytqoyC6wIVxcDACh1GiQlDEAQYASABEgIyu_D_BwE. [Accessed: 04-Aug-2020].
[9] U.S. Energy Information Administration, eia.gov, 2020 [online]. Available: https://www.eia.gov/outlooks/aeo/assumptions/pdf/table_8.2.pdf [Accessed 04 - Aug - 2020]
Acknowledgements
The Hopi Solar Capstone Team gives special thanks to: Karin Wadsack, Manager, Hopi Renewable Energy Office
Kendrick Lomayestewa, Manager, Hopi Renewable Energy Office
Fletcher Wilkinson, Energy Manager, Hopi Utility Corporation and
Senior Lecturer, David Willy and Professor David Trevas
Solar Powered: Currently, there are no power plants located on Hopi territory, making the tribe entirely energy dependent. Solar Energy is a clean, reliable step towards energy independence that takes advantage of the plentiful Arizona sunshine.
Reliable: The Hopi Tribe should feel confident in their energy, which means including battery storage to provide energy at night and during possible blackouts. This requirement also encompasses the development and sustainability of reliable jobs within the Hopi Tribe.
Durable: This power plant, if implemented, would be the only power plant on Hopi territory, so having it live a long and thriving life is important. The workers hired to maintain the equipment are essential towards increasing the power plant’s lifespan.
Safe: Job security includes physical safety on site. By reducing moving parts, the threat of employee injury reduces.
Cost Effective: The power plant needs to have low part expenses and have a quick turn-around on energy production to offset the costs of implementation and construction.
Requirements
Grid Design Layout
ABB Inverter Station: PVS800-IS-2MW
Solar Power Plant PV Module Layout
AEP and LCOE Results for Solar Plant Design
NX Gemini Racking and Tracking System
NX Gemini Bearing and Drive System Gaps for Bifacial Modules
Jinko Solar 445W Mono Bifacial PV Module
System Lifetime Energy Production
System Energy Loss Factors
Notes: Good content categories added (do not use the default content titles on the provided templates). At least one section will have an infographic (graph, chart, analysis results). Mandatory categories include: Abstract, Requirements, Results, Acknowledgements, and References. Other categories could include: Analysis, Data, Testing, Design Process, Iterations, Conclusions, Methods.
Some content included or at least blocked out to make it clear what will be presented in each section. Title, rough draft of abstract, and team members all added to poster.
Categories organized for ease of flow from left to right, top to bottom
Poster sections and text look aligned with each other in each column, formatted professionally, text looks like a good size for posters