## Slide 1: 2021 Baja SAE Design Review Briefing (DRB)
2021 Car Number(s)
Northern Arizona University
Validation AZ #21 / Knowledge #55
School Name

## Slide 2: OVERALL VEHICLE PRESENTATION
Goals
  Place top 5 in endurance
  5 hours of uninterrupted drive time excluding fuel stops
  Vehicle weight under 330lbs with the additional 4WD
  50% front bias weight distribution to improve front end handling
  8ft turning radius
  100 hours of testing prior to competition to validate designs
  100ft acceleration under 4.2s

## Slide 3: OVERALL VEHICLE PRESENTATION – GOALS AND REQUIREMENTS
Requirement | Design Target / Goal | Why this target was chosen | Result | Notes: (analysis, testing, additional details)
Curb Weight | 330lbs | Lightweight for maximized speed | 322lbs | 
Weight Bias Front / Rear | 50% front, 50% rear | Equal weight distribution maximizes steering and traction | 49.5% Front 50.5 % Rear | 
Overall Width (Outside edge of widest rims) | 61 in | Maximize stability | 61 front, 51 rear | Rear track width was decreased for improved steering and shock angles
Overall Height (ground to top of roll cage) | 62 in | Accommodate 4WD chain under seat with a 6ft driver. | 64in | 
Braking Distance | Full speed to full stop within 15 ft on asphalt | To be competitive in the braking test | 12 ft | 
Ground Clearance | 12 in | Handle off-road terrain without high center of gravity | 12 in | 
Tire Size | 23in diameter by 7 in wide | To achieve desired top speed | 23in diameter by 7in wide | 
Front Suspension Type | Unequal length double wishbone | Best overall reliability and performance | Unequal length double wishbone | 
Overall Suspension Travel (front and rear) | 8 in | Most used length of suspension travel | 8in | Potentiometer testing shows 5inches of average suspension travel used with an added 3 inches for harsh bumps
Rear Suspension Type | Upper link lower drive shaft (ULDS) | Improved ground clearance and weight reduction |  | Utilizes the rear axle held under axial forces as a camber link
Steering Wheel Rotations lock to lock | 2.5 rev | Most comfortable grip | 2.5 rev | 
Outside Turn Radius | 8ft | Improved maneuverability | 7.5 ft | 
Top Speed | 35mph | Competitive speed | 32mph | 
Acceleration Time (100ft, 150ft) | 4.2s |  | 4.4 s | 
Driveline Type (CVT, Sequential, CVT) | CVT | Lightweight and reliable | CVT | Quick change weights, ramps, and springs allow for fine tuning
4x4 Type | Chain | Lightweight and effective | Chain | Ratios/performance can be easily adjusted with different sprocket sizes. No differential assemblies needed
Vehicle Life Target (miles/hours) | 25 hours | Lightweight components while still allowing time for testing | 25 hours | 6 hours of drive time for competition, leaving 19 hours of drive time for testing
Key Features | Clutch part time 4wd | Reduces power loss | Part time 4wd | Under driven front axle with one-way clutch engages 4WD only when rear tires loose traction

## Slide 4: OVERALL VEHICLE PRESENTATION
Top View

## Slide 5: OVERALL VEHICLE PRESENTATION
Front View

## Slide 6: OVERALL VEHICLE PRESENTATION
Side View

## Slide 7: OVERALL VEHICLE PRESENTATION
Manufacturable light weight chassis design
  Utilizing 4130 Chromoly Steel; high strength to weight ratio
  Minimize unnecessary structural members and reach 65.6lbs chassis
  Reduce tube manufacturing time by eliminating bends occurring in multiple planes
Comfortable driving position for the driver
  Mounting the throttle and brake pedals convenient for feet comfortability
  Position and angle of steering wheel set between drivers' knees for greatest knee/hand clearance
  Added flange supports in seat to provide stress support in high force turns
  Integrate Shoulder-blade and hip support on seat for reduced sway of driver's body
Benchmarking/Testing previous vehicles(2019-2020)
  Stress analysis comparisons
  Data acquisition system used to collect loads with strain gauges for 2021 mathematical models
  Vehicle performance testing
Chassis and Ergonomics High Level Summary

## Slide 8: OVERALL VEHICLE PRESENTATION
Achieve 4WD overall system weight of under 45lbs
Sprag clutches in front hub to help with turning radius
Chain drive off 2WD gear box output allows vehicle to continue operating in the event of a 4WD failure
Under driven front shafts so that the 4WD only engages when rear wheels slip
Used dynamometer testing to measure the friction losses of the 4WD system
Gear box total weight of 8.2lbs, use of 9310 alloy and titanium allows for decreased size and weight
Drivetrain Sub-System Highlights
*CV Hub Assembly Section View
*4WD Side View
*Open Gear Box View
One-Way
Bearing
CV Spindle
Ball Bearing
Hub

## Slide 9: OVERALL VEHICLE PRESENTATION
Suspension and Steering High Level Summary
  Unequal length, double wishbone setup
  Upper mounted shocks with shock ratio of 2.25:1
  4130 Chromoly tubing control arms
  Billet 6061 Aluminum knuckles manufactured in-house
  8” total suspension travel
  50/50 weight bias over front and rear wheels
  15% increase in braking force from previous year NAU Baja vehicle
Rear Upper Link Lower Drive Shaft Design (ULDS)
Utilizes the Rear axles as a camber link
Machined 7075 aluminum rear bearing carriers
2 degrees camber gain
Notes: Steering/Brakes as separate slide

## Slide 10: OVERALL VEHICLE PRESENTATION
Steering and Brakes High Level Summary
Caliper for each wheel on front, single rear caliper directly mounted to gear box
Brake system testing included changing pedal ratio to see how it effects stopping performance
Infrared sensors mounted to knuckles to ensure brake fade wasn’t occurring over long runs.
12:1 Steering ratio resulting in 7.5 ft. turning radius
7075 steering rack due to increased cantilever loads from greater clevis eye to eye
Geometric points developed from Lotus were validated using a CMM after manufacturing
Notes: Steering/Brakes as separate slide

## Slide 11: 2021 Baja SAE Design Review Briefing (DRB)
2021 Car Number(s)
Northern Arizona University
Validation AZ #21 / Knowledge #55
School Name

## Slide 12: SYSTEM INTEGRATION
  Sources of Measurable Data
  Benchmarking using Previous NAU SAE Baja Vehicles
  Briggs and Stratton engine output graphs
  Dynamometer data
  Benchmark Testing Previous NAU SAE Baja Car #52
  Curb weight/Weight distribution
  Turning radius
  Acceleration
  Suspension testing
  Braking
  Vehicle Goals Set From Benchmarking
  Total Weight less than 330lbs, 30% lighter despite 4WD components
  Turning Radius less than 8ft, 33% smaller
  Braking to full stop in less than 12ft, compared to avg 25ft from previous NAU Baja cars
  50% front, 50% rear weight Distribution compared to 30%front, 70%rear from previous NAU Baja car
Benchmarking
Notes: Colton Lacey

## Slide 13: SYSTEM INTEGRATION
    Most research was performed from previous NAU vehicle designs.
    Potential designs prototyped on older chassis
    Ideas and motivation based off micro sprint dirt cars, UTV’s and ATV’s
    Literature Review for potential suspension mounting solutions
  What technologies or designs were available to help achieve the goal
    Documentation and feedback from previous years of SAE Baja vehicles at NAU
    Accelerometer testing data
    Industry support from Polaris, Ford Performance, Nissan, Allison Transmission, and Gates Engineering
    Strain gauge data from camber link suspension
    Material sample testing after heat treat using Instron
  Options considered (overall goal)
    Shape optimization on certain parts (weight savings)
    Used a steering rack that allowed more turning angle for the front wheels (increase turning radius)
    Higher pressure master cylinders improve braking force (decrease braking distance)
    Moved engine and cockpit forward (balanced weight distribution)
System Research
Notes: What type of support did you receive from industry?
For the System Research our primary source was from previous NAU baja vehicles and prototyping potential designs on previous chassis.
A lot of ideas and motivation came from micro sprint dirt cars as well as UTVs and ATVS. Multiple literature review provided potential suspension mounting solutions.
Some key factors which helped achieve our goal was documentation and feedback from previous teams, accelerometer testing, industry support from companies such as Polaris and Allision Transmission. We also performed strain gauge testing on a camber link suspension and material sample testing using a Instron testing machine to fully understand the affects of heat treating.
A few options that were considered for our overall goal was shape optimization on components to reduce a significant amount of weight
We also used quick ratio steering rack with a larger gear travel to obtain a larger turning radius. The other goal is positioning the engine and cockpit forward to obtain a balanced weight distribution.

## Slide 14: SYSTEM INTEGRATION
Component Selection Process
  Weighing pros and cons of each component design
  Decision Matrix for different options
  Consistent factor of safety throughout systems to avoid weak links
Component & Subsystem Selection
Component Category | Performance Factor (1-10) | Weight Factor (1-10) | FOS
Rotating components Rear only | 8 | 10 | 1.15
Control Arms | 7 | 4 | 1.1
Steering Components | 9 | 3 | 1.2
Driver Controls | 6 | 3 | 1.05
4WD system | 2 | 8 | 1.05
*Table of Factor of Safety
Selected subsystem components:
  Chain-driven four-wheel drive system
  Unequal-length double wishbone front suspension with CV joints
  ULDS rear suspension with Universal joints
  CVT Transmission
Notes: *Goal is constant factor of safety
Our component selection process included weighing the pros and cons for each component category and selecting the most appropriate design for the team. This was determined by assigning a performance factor which was based off how difficult the part will be to swap out in case of a failure, the other factor is a weight factor which is how much the weight will affect performance. Overall we strived for a constant factor of safety in each component category to ensure there is no weak links within the entire system.
The two options for providing a four-wheel drive system is a differential and a chain drive. We used a decision matrix to determine the chain drive system will be more appropriate for meeting the teams needs. We also used a decision matrix to select the proper rear suspension design concluding in the ULDS suspension.
The selected subsystem components was a front unequal double wishbone design, ULDS to eliminate a lower control arm in the rear suspension, and a CVT transmission.

## Slide 15: SYSTEM INTEGRATION
Subsystem Integration
U-joint Yoke to output shaft of gearbox using Innovative tapered screw to keep concentricity and resist cantilever loads
Yoke also has integrated rotor and sprocket mounts
RE relying on DT output for suspension geometry
Output Shaft
Chain Drive Sprocket
Outboard U-Joint Yoke
Flared Centering Screw
Rear Brake integrated into the gearbox casing eliminates the need for separate brake caliper mount
Integrated Gear Box and Rear Brake
Notes: One of the subsystem integration is using the rear half shafts as a suspension member for the hub and wheel assembly to maintain
proper geometry throughout suspension travel. That half shaft is also connected to the outboard U-joint yoke which is mounted to
the gear box using a flared centering screw to maintain concentricity while also resisting cantilever loads from the wheels.
Both outboard U-joint yokes also integrate as mounts for the driving sprocket and read brake rotor.
Another subsystem integration is the rear brake caliper mount which is positioned on the gearbox casing and eliminates the design
process of creating a separate brake caliper mount as well as weight reduction.

## Slide 16: SYSTEM INTEGRATION
Welded lateral mounting tabs optimized for specific loading case using shape optimization
Mounting locations for suspension were chosen to minimize frame members
Welded sleeves used as hinge points for rear suspension
Gear box mounting tabs laterally supported due to lateral forces from ULDS design
Integration solution to Frame

## Slide 17: SYSTEM INTEGRATION - Analysis
  Adams Car Simulator to evaluate front and rear suspension functionality and cohesiveness
  Vehicle loads based off dynamometer testing and drive tests with strain gauge data from previous NAU Baja vehicles
  Suspension Analysis Lotus Shark simulation software shows how different mounting locations effect suspension performance
Boundary conditions and loads:
  Load conditions based on previous teams' analyses and strain gauge data
  Suspension members analyzed using frame as fixed boundary condition
Component/Subsystem Integration Analysis
Component/Subsystem Integration Analysis
Analysis and Test Correlation:
Stresses on suspension members lower than predicted from FEA as frame strain absorbs some load from suspension members
Adams Car Simulator resulted in drastic performance improvement from extra 3in of rear suspension travel

## Slide 18: SYSTEM INTEGRATION
Subsystem/Vehicle Testing to meet goals:
    Dynamometer Testing
    Accelerometer
    Tensile strength testing on 4WD chain
Measurable data compared to measurable goals:
  Wheel horsepower and peak torque
  Rate of acceleration
  Length of chain stretch
Data Correlation:
  Drivetrain components could be optimized for the actual
  output of the engine and loads on vehicle
Test results impacting final design:
  Axle and drive shaft diameters were optimized to reduce weight and rotational inertia
Component/Subsystem Integration Testing

## Slide 19: SYSTEM INTEGRATION
The top goals our team did not meet were the distance to achieve top speed (a measure of acceleration) as well as the top speed itself.
  Root causes: Unforeseen drivetrain losses caused by the chain drive and sub-optimal CVT tuning
Our team achieved most of our top goals through selecting lightweight materials and by testing the limits of smaller components rather than selecting components with unnecessarily high factors of safety
Assessment Of Vehicle Goals
Top Vehicle Goals | Achieved Vehicle Goals
Total weight 330lbs | Total weight 322lbs
4WD vehicle | Chain-driven 4WD vehicle
25-hour vehicle life | 25-hour vehicle life
Top speed achieved within 25ft on asphalt | Top speed achieved within 27.7ft on asphalt
Top speed 35mph | Top speed 32mph
Turning radius 8ft | Turning radius 7.5ft

## Slide 20: 2021 Baja SAE Design Review Briefing (DRB)
Thank you
Questions?

## Slide 21: 2021 Baja SAE Design Review Briefing (DRB)
2021 Car Number(s)
Northern Arizona University
Validation AZ #21 / Knowledge #55
School Name

## Slide 22: CHASSIS / ERGONOMICS
Research and Development
Minimize unnecessary structural members in design to optimize weight reduction
Maintain frame structural integrity under high impulse forces
Secure driver in an ergonomic cockpit to provide safety
Requirements
4130 Chromoly Steel vs 1018 steel
  4130: Ultimate strength = 560 MPa
  Yield Strength = 460 MPa
  1018: Ultimate strength = 440 MPa
  Yield Strength = 370 MPa
Primary and Secondary member diameters
  Primary: 1.25” x 0.065”
  Secondary: 1.00” x 0.035”
Evaluated NAU’s previous designs for safety and cockpit ergonomics
  Seat comfortability
  Steering wheel distance and angle
  Mounting shear and placement
  Carbon Fiber panel development
Notes: Brendan Paulo

## Slide 23: CHASSIS / ERGONOMICS
Chassis CAD – Left Side View
Chassis CAD – Front View
Chassis CAD – Isometric View
Chassis CAD – Top View
Notes: Brendan Paulo

## Slide 24: CHASSIS / ERGONOMICS
Data Collection for Analysis
Loads collected from front and rear strain gauges attached to arms.
Forces applied to attachment points on chassis.
Accelerometer fixed to spare chassis members and dropped on concrete from 5ft.
4130 sample tested in Instron to gather modulus data.
Notes: Ashley Redmond

## Slide 25: CHASSIS / ERGONOMICS
Analysis Summary
Multiple Finite Element Analyses (FEA):
  Drop Test
  Front Impact Collision
  Torsion Test
  Rear Impact Collision
Equations used for simulated forces:
  + Error (drop test)
  + Error (front, rear, and side collisions)
Drop Test:
  Minimum factor of safety 1.102
  Greatest stress on RHO member
Front-End Collision:
  Minimum factor of safety 1.795
  Greatest stress on front upper A-arm
  member
Rear End Collision:
  Minimum factor of safety 1.157
  Greatest stress on mid rear
  members
Torsion Test:
  Minimum factor of safety 1.629
  Greatest stress on bottom rear members
Notes: Ashley Redmond

## Slide 26: CHASSIS / ERGONOMICS
Chassis Correlation of Analysis and Testing (or Plan)
Chassis Testing / Validation (or Plan)
Drive vehicle into cinder blocks at 14 mph using proper safety precautions
Drove last year's model at 14 mph into current model.
Drive vehicle off a 5-foot drop to test control arm mounting member integrity
Clamp frame onto table and jack up right side of chassis
Using motocross helmet, neck brace, safety overalls, seat harness, and body padding
Egress training
Produces a relative 2194lbf impulse force on front tow-point and to validate FEA results on bending, buckling, and displacement
Produces a 2194lbf impulse force on rear end
Produces a 2236lbf impulse force on RHO members
Produces torsional force on chassis
Notes: Brian Connors

## Slide 27: CHASSIS / ERGONOMICS
Must comfortably fit a 5th percentile female and a 95th percentile male while meeting all the minimum clearances
    Helmet must have a minimum 6in clearance
    Driver's shoulders, torso, hips, thighs, knees, arms, elbows, and hands must have a minimum 3in clearance
Driver must be able to exit either side of the vehicle within five seconds
Ergonomic Goals
Ergonomic Requirements
Design a unique, comfortable seat with flanges to laterally restrain the driver
    Carbon fiber material
Steering wheel should be further away from driver than previous years' designs
    Lightweight carbon fiber material
Brake/throttle pedals should be a comfortable distance from seat
Notes: Matthew Woodward

## Slide 28: CHASSIS / ERGONOMICS
Ergonomics Correlation of Analysis and Testing (or plan)
Ergonomics Testing / Validation (or Plan)
PVC pipe prototype of chassis
By averaging the team's hands size, we averaged at 8in long with an 8in circumference and constructed the steering wheel off this data
Seating all team members in the Seat mold
  Prior to creating the prototype composite seat
  Ensure it provides proper support
  By having the heaviest members of the team sit and bounce on the prototype we were able to gather data to prevent a future failure.
Version 1 seat failed under testing
  Plan to create finite element analysis simulation and mathematical model for seat failure and steering wheel failure
  Improve seat mounting geometry
Steering wheel performed well under heaving steering loads
  Driver felt comfortable for 2-hour duration
Notes: Matthew Woodward

## Slide 29: CHASSIS / ERGONOMICS
Ergonomics CAD – Left Side View
Ergonomics CAD – Front View
Ergonomics CAD – Isometric View
Ergonomics CAD – Top View
29 inches
44 inches
23 inches
Notes: Ashley Redmond

## Slide 30: 2021 Baja SAE Design Review Briefing (DRB)
2021 Car Number(s)
Northern Arizona University
Validation AZ #21 / Knowledge #55
School Name

## Slide 31: DRIVETRAIN Overview
Research and Development
4WD under 45lbs
4WD failure should not prevent RWD functionality
Decrease inertia by at least 20% from 2020 Chassis
Design the gearbox to weigh less than 9lbs
Have an acceleration of 100ft in <3.8s
Reduce vehicle rolling resistance by 4%
Chain drive significantly less weight than differential
Chain driven failure will be isolated off the output shaft delivering power to rear wheels
Gear box designed based off mathematical models to optimize strength and inertia
One-way clutches in front hubs allow for over rotation during turns
Under driven front shaft auto-engages 4WD when rear wheels slip
System Goals
CV Spindle
Deep Groove Ball Bearings
One-Way
Bearing
Splined Adapter
Sleeve
*CV Hub Assembly

## Slide 32: DRIVETRAIN - CVT
CVT Secondary Design
CVT Primary Design
10% reduction in weight 2.7lbs (2020)
Sheaves have 22% increase in surface area for better cooling
Quick change ramps & weights
Belt width increased for a better range: 3.3:0.5
Custom ramp geometry
16% reduction in weight 2.4lbs (2020)
Increased roller efficiency by disassembling and dry lubing
Axial limiter for pulling/climbing events
Custom helix profile with variable angle
Figure 2: Primary CVT Design
Figure 3: Secondary CVT Design

## Slide 33: DRIVETRAIN - CVT
CVT Modeling
CVT designed based off data from custom dynamometer
Weight and spring forces derived from target engagement (1350 RPM based off engine torque curve)
100 ft acceleration runs were conducted using 2020 vehicle with chassis mounted accelerometers, speed sensors and tachometer.
MATLAB was used to iterate ramp and helix geometries with a simple force diagram and centrifugal force equation.
Math model performs slip check using sheave clamp force and required wheel torque values
CVT design rationale/data collection for analysis
Primary Ramp
Quick Change Fly-Weight
Dry Lubed Roller
*CVT roller/ramp section view

## Slide 34: DRIVETRAIN - CVT
CVT / Transmission Correlation of Analysis and Testing
Lever Actuated CVT was made and tested to gather sheave force data though a spring scale for maximum torque output.
Future work includes:
  Mounting a data acquisition system to evaluate sheave position, RPM in and RPM out
  Sheave position will be monitored using linear potentiometer fixed to drive pulley.
CVT / Transmission Testing / Validation
Sheave force data was used to plug into MATLAB models which developed ramp profile geometry
Fly weights were then optimized to create adequate sheave force for expected driving conditions
Data from acquisition system will be used to determine when belt slippage occurs by knowing the sheave position which will give ratio. RPM out can be calculated from RPM in. With this data belt slippage can be minimized.
Run # | Max Sheave Force | Stall Load
1 | 287lbf | 14.22 ft*lb
2 | 309lbf | 15.65 ft*lb
3 | 356lbf | 16.12 ft*lb
*Table of CVT Test-Run Data

## Slide 35: DRIVETRAIN – Gear Box
Gear Box Design Rationale
8:1 Double reduction spur gears similar to previously successful 2WD box to keep engineering focused on 4WD system.
9310 Alloy gears case carburized to 63 HRC
4340M input shaft through hardened (52 HRC) to withstand cantilever load from CVT secondary
Titanium intermediate and output shaft to decrease overall and rotational mass
Gear internal geometries developed using topology optimization
8.2 lbs with fluid
Gear Box Overview
Ratio was determined by fixing a data acquisition system to a vehicle during a mock endurance race.
The average speed of 26 MPH was paired with a 1:1 CVT ratio (most efficient) to find 8:1.
The gear box assembly was designed for a 50-hour fatigue life cycle.

## Slide 36: DRIVETRAIN – Gear Box, Half Shafts and Hubs
Gear Box Cad Model Cut Away
Gear Box Half Shaft and Hubs CAD models
4340M Input Shaft
6AL4 TI Intermediate/output shaft
9310 Alloy Gears
7075 Al Case
4130 3-Piece Welded Half Shaft
Titanium Inboard Yoke
7075 Al Outboard Yoke and Hub

## Slide 37: DRIVETRAIN – Gear Box, Half Shafts and Hubs
Gear Box and Shafts Data Collection for Analysis
Gear, Half Shaft and Hub Analysis
Data was collected for using wireless strain gauges fixed to half shafts
  Torsional loads were collected under several conditions and max loading was seen during an asphalt drop test while vehicle wheels are at full speed. A load of 720 ft*lb was recorded
Strain Gauges were also attached to 2019 vehicle camber links to gather data for anticipated half shaft loads for new RE design
  Compressive loads were collected at high side impacts and tight highspeed corners. A max load on 1450lbf was recorded
Strain Gauges Fixed to Camber Links
Analysis was done by building AGMA mathematical models and FEA using loads from test data.
Fatigue life was set to 25 hours @ 25MPH based off completing two validation events without any component changes.
*FEA on Front Hubs
*FEA on Internal Gears

## Slide 38: DRIVETRAIN – Gear Box/Halfshafts
Gear Box/Half Validation & Analysis Correlation
Gear Box Iteration Changes
Laser cut .035” felt gasket installed between mating surfaces
Shafts turned down so aluminum spacer contacts inner race of bearings
Future work includes dye penetration testing on shafts and gears once 25 hours of run time has been hit.
2021 vehicle was subjected to same load conditions as 2019 vehicle data collection testing
Post validation inspection notes:
Gear Box leaked significantly out of sealing face
Aluminum shavings in oil from gear spacers rubbing on bearings
Gear face surfaces look free of pitting and wear
No signs of wear on U-Joint Yokes
Shafts and hubs re-measured for distortion using CMM

## Slide 39: DRIVETRAIN 4WD System
4WD Design Overview
Chain Drive System
  x4 7075 Aluminum sprockets anodized
  Sprockets mount to shafts using keyways and set screws
  Front Shaft: Titanium
  Intermediate Shaft: 7075 Aluminum
  Maneuverable pillow block clamps and chain tensioner for tension adjustment
  Sprag clutches used in front hubs to maintain turning radius and allow free spin
  Front shaft underdriven so front tires only engage when rear tires slip
Intermediate Shaft
Output shaft
Front Shaft
Front Shaft Section View:

## Slide 40: DRIVETRAIN 4WD System
Chain Drive Analysis Summary
Chain Drive
  Dynamometer testing, MATLAB, and drive testing from 2020 to calculate anticipated torque and chain tension on 4WD system using 450rpm and 10hp
Front/Intermediate Shafts:
  MATLAB used to calculate shaft diameters of 1.25" and 1.375" using 7075 aluminum and titanium
Chain System Calculations
  Chain Selection: 420nZ3 chain with tensile strength of 4,923lbs to satisfy anticipated forces
  Finite Element Analysis: Improved sprocket performance with different numbers of teeth using loads from data collection
    Ensured von Mises stress < yield strength
    Factor of Safety: 2.37
Chain Drive Data Collection for Analysis
Chain System #1
Chain System | Sprockets | Calculated Torque | Calculated Chain Tension
1 | 21 to 24 Teeth | 2,161 in-lbf | 1,288 lbf
2 | 15 to 18 Teeth | 2,161 in-lbf | 1,797 lbf
Chain System #2
Table 3: Chain System Calculated Results

## Slide 41: DRIVETRAIN 4WD System
Chain Drive Correlation of Analysis and Testing
Goal: Complete 4-hour endurance course under high loads without 4WD failure
Front Aluminum Shaft- System Failure Mode
  Shaft failed under stresses induced during high 8-degree hill climb and high shock testing at 18mph
Recreated failure mode and needed material with higher yield strength to support keyway
Titanium front shaft implemented for next design analysis, and did not fail during subsequent drive testing
Chain Drive/Half-Shaft Testing and Validation
Sprocket systems and chain linkages meshed efficiently for front tire spin during uphill climb in different terrains (i.e., snow, sand, gravel)
Confirmed chain performance through tensile strength testing and chain-stretch displacement
Confirmed center-to-center sprocket distances along body with assembly model measurements for tension
Validated new titanium front shaft with MATLAB shaft analysis factor of safety 1.8

## Slide 42: 2021 Baja SAE Design Review Briefing (DRB)
Questions?

## Slide 43: 2021 Baja SAE Design Review Briefing (DRB)
2021 Car Number(s)
Northern Arizona University
Validation AZ #21 / Knowledge #55
School Name

## Slide 44: SUSPENSION, STEERING AND BRAKES
Research and Development
Total suspension travel 8 in.
  6” travel in bump, 2” travel in droop in front
  5” travel in bump, 3” travel in droop in rear
Suspension mounting location for 50/50 weight bias
25% decrease in weight of suspension links
Target engineering requirements for Front-end geometry
Less than 3° camber gain over bump interval
5 ft. decrease in turning radius from previous year vehicle.
15% increase in braking force. (larger diameter rotors, higher pedal ratio)
Competitive Benchmarking with past NAU Baja Vehicles and top teams from past competitions
Lotus “Shark” suspension simulation used to create point cloud which was imported into SolidWorks
Literature review of academic sources
Initial Finite Element Analysis (FEA) and static force analysis on suspension components informed front control arm design.
Requirements

## Slide 45: SUSPENSION, STEERING AND BRAKES
Front Suspension – Left Side View
Front Suspension – Front View
Front Suspension – Isometric View
Front Suspension – Top View

## Slide 46: SUSPENSION, STEERING AND BRAKES
Steering CAD – Left Side View
Steering CAD – Front View
Steering CAD – Isometric View
Steering CAD – Top View

## Slide 47: SUSPENSION, STEERING AND BRAKES
Rear Suspension CAD – Left Side View
Rear Suspension CAD – Front View
Rear Suspension CAD – Isometric View
Rear Suspension CAD – Top View
ULDS design allows for relocation of wheel 1.4in behind chassis, distributes more weight to front tires for better weight distribution
Control arm forward mounts attach to roll hoop for added stability and resistance to axle wrap
Forward chassis mount clears transmission
Rear Shock mounted at rear bearing carrier hinge eliminating the need for a crossmember saving weight

## Slide 48: SUSPENSION, STEERING AND BRAKES
Brakes CAD – Rear Caliper
Brakes CAD – Front Caliper
Brakes CAD – Brake Rotor
Brakes CAD – Master Cylinders
Dual Piston
Free Floating
2.05-inch squared contact area
In-house Manufactured
Dual Piston
Free Floating
Utilizes same Brake Pads
Gearbox Mounted
Titanium Pistons
8-inch Diameter
0.12-inch Width
Titanium for Decrease Weight
.4-inch travel stroke
5/8-inch Bore
0.26 Lbs.

## Slide 49: SUSPENSION, STEERING AND BRAKES
Front Suspension and Steering Analysis Summary
Load cases measured with strain gauges mounted on prototyped Baja Vehicle
Lotus “Shark” suspension simulation used for iterative design and real-time kinematic curve generation
Front Suspension and Steering Data Collection for Analysis
Load cases applied to upper and lower control arms with Fusion 360 Finite Element Analysis (FEA) simulation
Performed shape optimization simulation on front knuckles to iterate design and reduce weight.
*Lotus Suspension Geometry
*Shape Optimization Analysis Results
*Finite Element Analysis Results
*Lotus Steering Geometry Analysis

## Slide 50: SUSPENSION, STEERING AND BRAKES
Rear Suspension Analysis Summary
Rear Suspension Data Collection for Analysis
Rear knuckle FEA:
Different load conditions tested based on strain gauge analyses
  Three main load conditions determined: impact from below, impact from front, impact from behind
Design iteratively adjusted to save weight with a target factor of safety of 1.0.
Rear knuckle:
Minimum factor of safety of 1.21
Weight reduced from 2.56lbs to 1.07lbs
Geometry Analysis:
-2 degrees of camber gain as suspension droops, creates wider track width during loss of contact with ground as modeled in lotus
*Rear Knuckle FEA Analysis
*Lotus Rear Suspension Simulation

## Slide 51: SUSPENSION, STEERING AND BRAKES
Brakes Analysis Summary
Infrared sensors fixed to knuckle in order to find rotor operating temp
  Maximum temp seen during a progressive downhill stop
  335F
2019 vehicle prototyped adjustable pedal ratio to find optimum pedal pad travel vs pedal force to lock wheels
Brakes Data Collection for Analysis
Performed thermal stresses study to evaluate brake performance under mechanical and thermal loading
Pedal Ratio | Measured pedal travel @ toe location | Measured Force to Lock
6:1 | 2.625” | 84lbf
7:1 | 3.125” | 62lbf
8:1 | 3.625” | 43lbf
*Table of Pedal Ratio Testing Results
*Brake Thermal Analysis
*Brake Thermal Stresses Analysis

## Slide 52: SUSPENSION, STEERING AND BRAKES
Front Suspension and Steering Correlation of Analysis and Testing (or Plan)
Front Suspension and Steering Testing / Validation (or Plan)
Geometry measurements using Coordinate-measuring Machine (CMM) post-manufacturing re-evaluated in Lotus Shark.
Shocks and springs testing conducted with DAC system using mounted potentiometers to measure displacement.
Ackerman steering geometry tested using adjustable pick-up points on front knuckle of 2018 Baja vehicle to find optimal geometry.
Front Suspension Static Values Achieved Post-manufacturing
  0.00° Camber (Identical to target value)
  2.08° Castor (4% difference from analytical model)
  14.46° Kingpin (3.6% difference from analytical model)
Measured Dynamic Steering Value
  4.75” steering rack travel at 12:1 ratio
  7.5’ turning radius with custom underdriven chain drive system (.5' improvement over analytical model)

## Slide 53: SUSPENSION, STEERING AND BRAKES
Brakes Correlation of Analysis and Testing (or Plan)
Post-manufacturing, real world testing conducted to validate design and analysis
Baja Vehicle subjected to 15 consecutive brake lock-up tests after accelerating 100ft
  Brake system passed lock-up test for all four wheels 13 out of 15 times with a success rate of 86.6%
  Max brake temp as measured after final trial was 238° F
Brake distance was also measured during the 15 trials to test braking performance under thermal stresses.
Brakes Testing / Validation (or Plan)
Testing revealed possible improvements to the braking system:
  Remanufacturing brake pedal assembly to avoid brake reservoir lines
  Brake hard line rerouting to avoid driver's feet
Floating rear brake caliper seized on first test due to tight tolerances of titanium piston moving in the caliper bore
  Newly machined pistons with .001” of clearance fixed binding problem
*Braking Distance Testing Results
*Seized Rear Brake Caliper

## Slide 54: SUSPENSION, STEERING AND BRAKES
Rear Suspension Correlation of Analysis and Testing (or Plan)
Rear Suspension Testing / Validation (or Plan)
Measuring strain on control arms:
  Validates FEA
  Subjects suspension components to actual load conditions
  Allows team to more accurately analyze components
Static gearbox testing:
  Ensures gearbox and rear suspension integrity
  Validates FEA
Because the gearbox and axles act as suspension components, they must be able to withstand the same loads as suspension members as well as transferring power to the rear wheels
Strain Gauges attached to rear arm during test driving
Plan to static-test inboard gearbox yokes to measure deflection of gearbox under axial forces
Plan to perform axial-load and torsional-load test on rear half shaft to validate FEA

## Slide 55: 2021 Baja SAE Design Review Briefing (DRB)
Questions?