## Slide 1: P5-NPOI Fina Testing Results
Bradley Kingsley
Dustin Haines
Trung Son Nguyen

## Slide 2: Design Requirements Summary
Create an Updated Vacuum Interface:
  Lightweight (CR #1)
  Adjustable Components (CR #4)
  Small Deformations – Optical Standard (CR #5)
  Ability for interior Access in Vacuum State (CR #7)
  NEW – Prototype Allows Light in & Out Unclipped (CR #8)
CR's 2,3, & 6:
  Unable to complete due to deliverable modification in Jan. 2023
  CR/ER #2 – Disassembly in less than 1 hour
  CR/Er #3 – Seals to Vacuum and ATM
  CR/ER #6 – Drift Less than 0.001" Per Month
Haines 1

## Slide 3: Top Level Testing Summary
Experiment/Test | Relevant Design Requirement
Front Seal Plate Weight | CR/ER 1
Rear Seal Plate Weight | CR/ER 1
Front Seal Plate Deflection | CR/ER 5
Rear Seal Plate Deflection | CR/ER 5
Snoot Plate Adjustment | CR/ER 4
Snoot x/y Adjustment (combined) | CR/ER 4
Rear Seal Plate Sight Port Count | CR/ER 7
Allow Laser in & out of Scaled System | ER 8 (NEW, allow light into and out of the system without clipping. Allow full adjustment of parts)
Nguyen 2

## Slide 4: Test #1 & #2 – Seal Plate Weight
Verify Weight of 3D Model in SolidWorks
Use Material Spec. Sheet given by material supplier for density
Verify Weight with equation:
  Weight = Volume * Density
Weight Must be Below 35 Pounds
  Front & Rear
F: 34.2 pounds
R: 33.9 pounds
Haines 3

## Slide 5: Test #3 & #4 – Seal Plate Deflection
Use of SolidWorks and ANSYS Workbench
Apply Material properties (6061-T651):
  Poisson's Ratio
  Modulus of Elasticity
  Etc.
Apply Boundary Conditions:
  Rear Holde Edge Fixed Conditions (zero deflection)
  Front 16" Diameter Circle Standard ATM Pressure (14.7 PSIA)
    Corrected for local attachments applying greater pressure on Annulus
F: 0.00373"
R: 0.00492"
Kingsley 4

## Slide 6: Test #5 – Snoot Plate Adjustment
Nguyen 5
Use the from seal plate assembly to measure deltas in x & y
  Bring to y-min and take reference measurement
  Bring to y-max and take measurement
  Calculate the delta distance as the single direction adjustability
  Repeat for the x-direction
Required adjustments are 35% of the full scale
  Δprototype = Δfullscale * 0.35 = 0.175"
  Δfullscale = 0.5°
Outcome: Δprototype, found x & y = ± 0.190"

## Slide 7: Test #6 – Snoot X/Y Adjustment
Christmas Tree and Snoot Adjustment Combined Adjustment
  Christmas Tree Vertical found:
    Max – Min = Adjustment Length
    Found Bilateral Length of adjustment = ±0.3125” = ± 5/16”
  Snoot Adjustment Plate Vertical:
    Max – Min = Adjustment Length Addition
    Found Bilateral Length of Adjustment = ± 0.125” = ± 1/8”
  Snoot Adjustment Plate Horizontal:
    Max – Min = Adjustment Length
    Found Bilateral Length of Adjustment = ± 0.125” = ± 1/8”
  Full Vertical Range = 0.4375” = 7/16”
  Full Horizontal Range = 0.125” = 1/8”
Nguyen 6

## Slide 8: Test #7 – Rear Seal Plate Sight Port Count
How Many Poly-Carbonate Vacuum Windows Can be Attached to the Rear Seal Plate?
  Count = 0-3 Windows Can Be Attached
  All Ports Have the Same Bolt Patter and O-Ring
  There are 3
Haines 7

## Slide 9: Test #8 – Laser In/Out Unclipped in Prototype
Use 2x KM1CE Thorlabs Mirror Mounts
Develop a Fixed Mount for attaching Mounts in Correct Center Location
Align the Mirror Mounts to Allow Light In and Out of the Prototype
Criteria: Is the beam able to enter and exit unclipped by the prototype assembly?
Kingsley 8

## Slide 10
The laser test worked
The laser comes from the snoot stand, reflected by the mirror system and comes back through lower snoot
VIDEO
Test #8 – Laser In/Out Unclipped in Prototype
Haines 9

## Slide 12: Specification Sheet
Customer Requirement | CR met (Y/N) | Client Acceptable (Y/N)
CR1 - Lightweight | Y | Y
CR2 – User/Technician Friendly | Y | Y
CR3 – Seals to Vacuum | N/A | Y
CR4 – Stable Alignment | N/A | Y
CR5 – Small Deformations | N/A | Y
CR6 – Adjustable Frame | Y | Y
CR7 – Sight Ports | Y | Y
CR8 – Allow Laser Light In/Out of the System | Y | Y
Haines 10

## Slide 13
Engineering Requirement | Target | Tolerance | Measured Value | ER Met? | Client Acceptable?
ER1 – SP Less than 35 pounds | <35 lbs. | ±0.5 lbs. | Front- 34.2 lbs. Rear- 33.9 lbs. | YES | YES
ER2 – Disassemble in < 60 minutes | < 60 minutes | ±5 min. | N/A | N/A | YES
ER3 – Seals Tank in Vacuum and ATM | Seals Tank | N/A | N/A | N/A | YES
ER4 – X-Y Adjustment of ±0.5” (Scaled @ 35% =0.175”) | ±0.0875” or greater | ±0.010” | -VERTICAL TREE= ±0.3125” -PISTON STAND=N/A -VERTICAL PLATE= ±0.125" -HORIZONTAL PLATE= ±0.125" -SNOOT PLATE= ±0.10” -SNOOT PISTON= ±0.125” * ± Value Given as ½ of Full Range of Adjustment. | YES | YES
ER5 – SP Deformation < 0.01” | <0.010” | ±0.0001” | Front- 0.00373” Rear- 0.00492” | YES | YES
ER6 – Drift less than 0.001 in/month | < 0.001 in/month | ±N/A | N/A | N/A | N/A
ER7 – 2+ Sight Ports | 2+ Windows | No Tolerance | 1-3 available for use. | YES | YES
ER8 – Unclipped Laser through system | Unclipped Laser Beam | N/A | Unclipped | YES | YES

## Slide 14: QFD
Haines 12

## Slide 15: Question or Comments?