## Slide 1: Novel hobby scale powder coating oven with active controls for future student engineering projects
Verina Abdelmesih
Hussain Alismail
Desiree Dee

## Slide 2: Project Description
Goal
Design a powder coating oven that can be used by all programs
Work with the bumper capstone team
Powered by a propane fueled torpedo heater
Controlled using a PID control system
Stakeholder
The Renewable Energy Lab
Client
Carson Pete
The powder coating machine will be housed in the renewable energy lab
Hussain 1

## Slide 3: Background
What is Powder-Coating?​
It’s the process of applying fine, pigment particles that are electrically charged and sprayed onto the part.​
What projects can you do with powder coating?​
It could be applied from Simple DIYs to high end industrial applications.​
Powder-Coating ovens?​
The last step for powder coating to cure the powder onto the part.​
Hussain 2

## Slide 4: Design Description
Oven Body
Rack System
Torpedo Heater
PID System
Exhaust Vent
Hussain 3

## Slide 5: Design Requirements
Engineering Requirements:
ER 1: Rack Holding Weight < 200 pounds
ER 2: Volume (4 x 4 x 8ft)
ER 3: Material Cost < $1,500
ER 4: Heat Loss < 6 W/m^2
ER 5: Heat Output of 400° Fahrenheit
Customer Requirements:
CR 1: Weather Resistant
CR 2: Even Heat Distribution
CR 3: Material Cost < $1,500
CR 4: Volume (4 x 4 x 8ft)
CR 5: Retractable Rack System
CR 6: Propane Fueled Heater
CR 7: Control System for Heater
Hussain 4

## Slide 6: Decision Matrix
Hussain 5

## Slide 7: Design Analysis : Structural Analysis
Snow Load Analysis:
Snow Load = 11.435lbs/ = 183lbs
Exposure Factor, 0.8 or 0.9
Thermal Factor, 1.1
Importance Factor, 1.1
Minimum Snow Load, 15lbs/
Hussain 6

## Slide 8: Design Analysis: Structural Analysis
Factor of Safety:
FOS =
Materials:
1.5” Steel Square Tubes
FOS Required:
1.5
Max Weight Used:
225lbs
Hussain 7

## Slide 9: Design Analysis/Prototype 1/Testing plan 2 : Heat Transfer Analysis
Desiree 8

## Slide 10: Design Validation: FMEA
Desiree 9

## Slide 11: Prototype 2: Powder Coating Technique
Prep/Pretreatment
Use Super Degreaser to clean the part
Blast/Sand down the object to remove impurities
Use AllPrep Iron Phosphate
Use an Epoxy base coat and cure for longer
than powder curing time
Application
Ground part using a wire
Note Faraday areas
Preheat part with oven to improve adhesion

## Slide 12
Desiree 11

## Slide 13: Manufacturing Plan
Calculate and measure the distance of the rivet on the oven frame.
Cut out holes in the door sheet panels for the tempered glass.
Rivet interior sheet metal to each framing
Rivet the framing of the oven together excluding the door.
Create the frame of the door. Include a frame for the tempered glass so that it doesn’t contact insulation.
Assemble oven frame with sheet metal
Measure the holes in the cold-rolled steel panels for the heater, vent, and blower.
Desiree 12

## Slide 14: Manufacturing Plan Pt. 2
9. Cut the top inside panel of the oven wall for the light placement. Then make the holes for the burner and the vent.
10. Add the insulation. Then add the wiring for the thermocouple and light bulb along with the light bulb mount to the oven
11. Then attach the outer panels of the oven and paint with high temperature Rust-oleum.
12. Cut the holes of the vent and heater on the outer panels of the oven
13. Attach the door to the oven using piano hinges and latches
14. Attach the control system, vent, and heater to the oven
Desiree 13

## Slide 15: Manufacturing Process
Desiree 14

## Slide 16
Desiree 15

## Slide 17
Wire Color Key
  Alarm : Red
  Alarm Switch : Black
  Light : Pink and Cream
  Heater : Green
  Terminal to Terminal : White
  Terminal to SSR : Blue
  Anything to Connector : Yellow
Verina 16

## Slide 18
Verina 17

## Slide 19: Test 3: control system
Design requirements​
  ER5: Heat output of 400 degrees ​
  CR2: Even Heat Distribution​
  CR6: Propane Fueled Heater​
  CR7: Control System for Heater
Verina 18

## Slide 20
Verina 19

## Slide 21: Test 4: Heat Ventilation and circulation
Design requirements:​
  ER5: Heat output of 400 degrees F ​
  CR2: Even Heat Distribution​
  CR6: Propane Fueled Heater​
  CR7: Control System for Heater​
One Coat
Two Coats​
Verina 20

## Slide 22: Test 5 : Curing techniques on rack
Design requirement
  CR2: even heat distribution
  CR5: retractable rack system
Verina 21

## Slide 23: Test 6: Rack System weight test
Design requirements
  ER1: Rack holding weight < 200 lbs
  CR5: Retractable rack system
Verina 22

## Slide 24: SPECIFICATIONS SHEET: CUSTOMER REQUIREMENTS​
Verina 23

## Slide 25: SPECIFICATIONS SHEET: ENGINEERING REQUIREMENTS

## Slide 26: Future Work
Improve vent system
  Sync vent to PID so that it open and closes when the oven reaches certain temperatures instead of heater turning on and off
  Will allow for oven to be more fuel efficient
Verina 24

## Slide 27: Questions?
Please feel free to visit our website!

## Slide 28: References
[1] Basic instructions, https://www.columbiacoatings.com/resources/basic-instructions (accessed Nov. 2, 2023). ​
[2] “How to build a PID controlled toaster oven | full guide | round 2,” YouTube, https://www.youtube.com/watch?v=PuoiD9mwmUQ​
(accessed Nov. 2, 2023). ​
[3] S. Castle, “How to build a powder coating oven,” Powder Coating: The Complete Guide, https://www.powdercoatguide.com/2014/09/how-to-build-powder-coating-oven.html (accessed Nov. 2, 2023). ​
[4]S. Castle, “How to build a powder coating oven part ii,” Powder Coating: The Complete Guide, https://www.powdercoatguide.com/2014/09/how-to-build-powder-coating-oven-part-ii.html#.WLn0GH-mLWB (accessed Nov. 2, 2023). ​
[5] Name, B. M. says:, S. says:, A. V. says:, and G. W. I. says:, “Engineer Essentials LLC - creators of GD&T Basics,” GDT Basics, https://www.gdandtbasics.com/asme-y14-5-gdt-standard/ (accessed Nov. 2, 2023).​
[6] “Factors of safety - fos,” Engineering ToolBox, https://www.engineeringtoolbox.com/factors-safety-fos-d_1624.html (accessed Nov. 2, 2023).​

## Slide 29
[7] Northern Arizona University, "ME 495 – Intro to Data Acquisition with NI & Arduino," Flagstaff, AZ, 2022 ​
[8] “Mineral Wool Insulation,” Engineering ToolBox. [Online]. Available: https://www.engineeringtoolbox.com/mineral-wool-insulation-k-values-d_815.html. [Accessed: 30-Apr-2023]. ​
[9] Dan, “Calculating the developed length of a rolled cylinder,” The Chicago Curve, 22-May-2016. [Online]. Available: https://www.cmrp.com/blog/plate-rolling/calculating-the-developed-length-of-a-rolled-cylinder.html#:~:text=The%20AutoCAD%20default%20K%20value,your%20software%20to%20K%20%3D%200.50. [Accessed: 30-Apr-2023]. ​
[10] “Convection heat transfer coefficient,” Convection Heat Transfer Coefficient - an overview | ScienceDirect Topics. [Online]. Available: https://www.sciencedirect.com/topics/engineering/convection-heat-transfer-coefficient. [Accessed: 30-Apr-2023]. ​
[11] “Calculating roof snow loads w/ ASCE 7-10: Skyciv,” SkyCiv Cloud Structural Analysis Software | Cloud Structural Analysis Software and Calculators, https://skyciv.com/docs/tech-notes/loading/calculating-roof-snow-loads-w-asce-7-10/ (accessed Nov. 16, 2023)