## Slide 1: Final Testing Results By: Brandon Knutson, Daniel Cooke, Mica Nellis Mason Goodman, Russel Stringham, Isaiah Padilla

## Slide 2: Design Requirements Summary
Customer Requirements:
CR1 - Working Volume (50” D x 4’ Height)
CR2 – ¼” Aluminum Drilling
CR3 - Human Input Responsive (HIR)
CR4 – 0.003” Drilling Tolerance
CR5 – Portable
CR6 – Electrical Power
CR7 – Emergency Stop
CR8 – Cost Efficient
Engineering Requirements:
ER1 – Deflects < 0.1” During Drilling
ER2 – Spindle Speed 3,000 RPM
ER3 – Motor Torque 100 N-m
ER4– Human Input Responsive
ER5 – Assembly < 150 lbs

## Slide 3
TOP LEVEL TESTING DESIGN SUMMARY |  |  |  |  |  |  |  |  |  |  |  | 
Test Plan |  |  |  |  |  |  |  |  | Test Report |  |  | 
Specification | Unit Under Test | Test Description | Relevant DR's | Acceptance Criteria | Target Requirements | Test Responsibility | Test Equipment | Est. Completion | Act. Completion | Test Notes | Pass/Fail | Course of Action
J1 - J6 Motor Amperage | J1 - J6 Motors | Provide varied "Loads" in the form of hand resistance up until shortly before stall torques to understand general amperage pull compared to that of rated currents for each motor | CR 6 – Electrical Pwr CR 7 – Emergency Stop | Motors do not exceed an amperage reading of 10 A to ensure protection of J1 - J6 Motor Drivers | All Must Pass | Mica / Brandon | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Arduino Software | 8-April | 7-April | Power, efficiency, amperage, behaved as expected | Pass | N/A
Spindle Wiring & Rpm | End Effector | Wire the end effector in unison with the Varaible Frequency Drive to ensure purchased wiring is adequate and the Rpm's of the end effector can be adjusted | CR 2 – ¼ “ Al Drilling CR 7 – Emergency Stop ER 2 - Spindle Speed | End effector runs and has variable Rpm capabilities for wood/aluminum to guarantee future testing capabilities | All Must Pass | Mica / Brandon | 10 A Spindle, VFD, Variable Power Supply, AWM 2586 Wire | 8-April | 8-April | Spindle speed was able to reach the desired 3000 rpm with 50 Hz of power | Pass | N/A
Refined Joint Displacement | Complete Robotic Design | Robotic design can move in the X,Y, and Z planes as intended | CR1 - Working Vol CR2 – ¼” Al Drilling CR3 - HIR CR4 – Drilling Tolerance CR5 – Portable CR6 – Electrical Power CR7 – Emergency Stop CR8 – Cost Efficient ER1 – Deflects < 0.1” ER2 – Spindle Speed ER3 – Motor Torque ER4– HIR ER5 – Assembly < 150 lbs | Joints can complete task movements at various extensions for 10 minutes | Minimum Viable Product | Whole Team | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Limit Switches, J1 - J6 Manufactured Parts, Roller Dolly, Complete Hardware, Arduino Software | 16-April-19-April | 25-Mar - 9-April | All motors behave as expected with the exception of J2 | Pass | N/A
Real World Simulation | Complete Robotic Design | A real world simulation where the design moves in multiple planes & completes drilling operations | All - Reference Above | Movement is continuous & complete with a finished drilling operations that meets CR's | Minimum Viable Product | Whole Team | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Limit Switches, J1 - J6 Manufactured Parts, Roller Dolly, Complete Hardware, Arduino Software | 23-April | 9-April – 22 - April | Robot behaved as needed and completed acts of drilling | Pass | Refine precision movement

## Slide 4
Testing Plan – Torque Speed Curves
Set Speed and delivered step pulses with an Arduino Micro.
Tested Motors with weights for a range of speeds
Repeated with the motor and Gearbox and just the motor.

## Slide 5
Testing Plan – Power Efficiencies
Values for 15 to 180 RPM | Motor W/ Gearbox | Motor W/O Gearbox | Stepper Online Data Sheet
Average Torque (NM) | 6.82 NM | 0.7871 | 5.70
Peak Power (Watts) | 121 | 14.8 | 66.75
Theoretical Motor W/ Gearbox output: 7.871 NM
Found Motor W/ Gearbox output: 6.82NM
Our Findings...
2 stage Gearbox efficiency is 87%
3 stage Gearbox efficiency is 81%
Stepper Online States
2 stage Gearbox efficiency is 85%
3 stage Gearbox efficiency is 75%

## Slide 6: Detailed Testing Plans: Input Power vs Efficiency

## Slide 7
Testing Plan – Spindle Speed
Chart: VFD Power Output vs. Spindle Speed
| 0 | 10.1 | 20.100000000000001 | 30.1 | 40 | 50.4 | 59.9 | 70.5 | 80.3 | 90.4 | 100
 | 0 | 591.6 | 1204.7 | 1808.2 | 2535.7 | 3029.4 | 3574.7 | 4228.1 | 4856.9 | 5325.5 | 6017.1
Summary:
Wire the end effector in unison with the Variable Frequency Drive (VFD) to ensure purchased wiring is adequate and the Rpm’s of the end effector can be adjusted
Testing ER2 - Spindle speed of 3000 RPM
Procedure:
Power on VFD to 10 Hz increase in increments of 10 until 100 Hz is reached
Measure spindle speed in rounds per minute (RPM) at each increment
Verify that 50 Hz outputs 3000 RPM
Results: Pass

## Slide 8: Testing Plans VFD Power and Spindle Speed

## Slide 9
Testing Plan – Refined Joint Displacement
Goals
Document tendencies of individual joints while moving
Determine ideal settings within the programmable software
Identify points of failure for each moving joint
Materials Required: Robot Assembly, AccelStepper for Arduino IDE, properly wired and coded motor drivers.
Procedures
Determine the desired range of motion required for each joint to move while maintaining the working volume.
Calculate the required microsteps from the individual motor's pulse per revolution setting, gear box ratio, and second stage reduction ratio.
Write code within AccelStepper to loop an individual motor at the desired speed and travel settings.
Beginning with J1, measure angular displacement and document irregular movement, stalling, and potential points of joint failure
Once desired range of motion has been achieved for each individual motor, repeat step for while operating two joints in unison.
Repeat until all four motors can move in unison without failure.

## Slide 10
Testing Plan – Real World Simulation
Goal: Robot will perform drilling operation at eight predetermined locations.
Requirements Tested
CR1: Working Volume
CR2: Drills Through ¼’’ Aluminum
CR3: Human Input Responsive (HIR)
CR4: .003’’ Drilling Tolerance
ER1: Deflects < 0.1’’ During Drilling
ER2: Spindle Speed: 3,000 RPM
ER3: Motor Torque: 100 N-m
ER4: HIR
Materials Needed
Complete Assembly of Robot
(2) ¼’’ Aluminum Plates
Testing Jig
Arduino Program
Procedures
Secure aluminum plates to testing jig, one at a height of 2 foot from the ground, the other at a height of 4 feet.
Write IDE code that controls the end effector.
Establish a square bolt hole pattern for each plate, with each hole being 1.5 inches apart.
Set spindle speed to 3,000 rotations per minute.
Reset robot joints to “home” location.
Run program.
Expectations
Robot should be able to perform entire drilling operation without any human interference once the program has commenced.
Four holes should be drilled at the expected locations in each plate with little error.
Team will document time to complete operation, significant deflections, and any error with the movement of each joint.
Test will be conducted until the results are customer acceptable.

## Slide 11
Testing Plan – Real World Simulation
Results
Average time to reach desired location from home position: 35.8 seconds
Average time to drill: 94.4 seconds
Drill bit: 1/8’’
Spindle speed: 5000 rpm
Human input responsive to ¼’’ precision
Issue
Lack of desired precision
Inconsistencies with motor speed and displacement
Drill bit deflection upon impact with aluminum
Cannot move horizontally and drill on flat plate
Once hole is complete, drill bit resists removal from aluminum plate

## Slide 12
Specification Sheets – Customer Requirements
Customer Requirement | CR met (Y/N) | Client Acceptable (Y/N)
CR 1 - Working Volume (50" D, 4' Height ) | Yes | Yes
CR 2 - 1/4" Aluminum Drilling | Yes | Yes
CR 3 - Human Input Responsive | Yes | Yes
CR 4 - .003" Drilling tolerance | No | TBD
CR 5 - Portable | Yes | Yes
CR 6 - Electric Power | Yes | Yes
CR 7 - Emergency Stop | Yes | Yes
CR 8 - Cost Efficient | Yes | Yes

## Slide 13
Specification Sheets – Engineering Requirements
Engineering Requirement | Target | Tolerance | Measured Value | ER met (Y/N) | Client Acceptable (Y/N)
ER 1 - Deflects < .1'' during drilling | .1'' | -.1'' | .25” | No | TBD
ER 2 - Spindle Speed 3000 Rpm | 3000 RPM | +/- 200 RPM | 3029.4 RPM | Yes | Yes
ER 3 - Motor Torque 100 N-m | 100 N-m | +/- 2 N-m | +/- 2 N-m | Yes | Yes
ER 4 - Human Input Responsive | Yes | N/A | N/A | Yes | Yes
ER 5 - Assembly < 150 lbs | 150 Lbs | +/- 10 Lbs | ~ 110 lbs | Yes | Yes

## Slide 14: Quality Function Deployment

## Slide 15: Assembly

## Slide 16: Final Product Demo