## Slide 1: Initial Testing Results By: Brandon Knutson, Daniel Cooke, Mica Nellis Mason Goodman, Russel Stringham, Isaiah Padilla

## Slide 2: Design Requirements Summary
Customer Requirements:
CR1 - Working Volume (50” D x 4’ Height)
CR2 – ¼” Aluminum Drilling
CR3 - Human Input Responsive (HIR)
CR4 – 0.003” Drilling Tolerance
CR5 – Portable
CR6 – Electrical Power
CR7 – Emergency Stop
CR8 – Cost Efficient
Engineering Requirements:
ER1 – Deflects < 0.1” During Drilling
ER2 – Spindle Speed 3,000 RPM
ER3 – Motor Torque 100 N-m
ER4– Human Input Responsive
ER5 – Assembly < 150 lbs

## Slide 3
TOP LEVEL DESIGN SUMMARY |  |  |  |  |  |  |  |  |  |  |  | 
Test Plan |  |  |  |  |  |  |  |  | Test Report |  |  | 
Specification | Unit Under Test | Test Description | Relevant DR's | Acceptance Criteria | Target Requirements | Test Responsibility | Test Equipment | Est. Completion | Act. Completion | Test Notes | Pass/Fail | Course of Action
J1 - J6 Motor Amperage | J1 - J6 Motors | Provide varied "Loads" in the form of hand resistance up until shortly before stall torques to understand general amperage pull compared to that of rated currents for each motor | CR 6 – Electrical Pwr CR 7 – Emergency Stop | Motors do not exceed an amperage reading of 10 A to ensure protection of J1 - J6 Motor Drivers | All Must Pass | Mica / Brandon | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Arduino Software | 8-April | 7-April | Power, efficiency, amperage, behaved as expected | TBD | Need to measure torque values to plot torque vs speed
Spindle Wiring & Rpm | End Effector | Wire the end effector in unison with the Varaible Frequency Drive to ensure purchased wiring is adequate and the Rpm's of the end effector can be adjusted | CR 2 – ¼ “ Al Drilling CR 7 – Emergency Stop ER 2 - Spindle Speed | End effector runs and has variable Rpm capabilities for wood/aluminum to guarentee future testing capabilites | All Must Pass | Mica / Brandon | 10 A Spindle, VFD, Variable Power Supply, AWM 2586 Wire | 8-April | 8-April | Spindle speed was able to reach the desired 3000 rpm with 50 Hz of power | Pass | N/A
Modular Electrical | J1-J6 Motors, Power Supply, Joint Manufactured Equipment | Assemble the robotic arm in a "ground up" manner ensuring that manufactured equipment "fits" as intended and electrical power can be supplied to jog motors at each joint level | CR 1 – Working Vol. CR 3 - HIR CR 5 - Portable ER 5 – Assembly Weight | Design can be assembled as intended & motors can jog at each respective joint level | All Must Pass | Whole Team | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Limit Switches, J1 - J6 Manufactured Parts, Roller Dolly, Complete Hardware, Arduino Software | TBD |  |  | TBD | 
Refined Joint Displacement | Complete Robotic Design | Robotic design can move in the X,Y, and Z planes as intended | CR1 - Working Vol CR2 – ¼” Al Drilling CR3 - HIR CR4 – Drilling Tolerance CR5 – Portable CR6 – Electrical Power CR7 – Emergency Stop CR8 – Cost Efficient ER1 – Deflects < 0.1” ER2 – Spindle Speed ER3 – Motor Torque ER4– HIR ER5 – Assembly < 150 lbs | Joints can complete task movements at various extensions for 10 minutes | Minimum Viable Product | Whole Team | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Limit Switches, J1 - J6 Manufactured Parts, Roller Dolly, Complete Hardware, Arduino Software | TBD | 25-Mar - 9-April | All motors behave as expected with the exception of J2 | Pass | Make adjustments to J2 motor assembly
Real World Simulation | Complete Robotic Design | A real world simulation where the design moves in multiple planes & completes drilling operations | All - Reference Above | Movement is continuous & complete with a finished drilling operations that meets CR's | Minimum Viable Product | Whole Team | J1 - J6 Motors, Variable Power Supply, 10 A Motor Driver, 20 AWG wire, AWM 2586 Wire, Limit Switches, J1 - J6 Manufactured Parts, Roller Dolly, Complete Hardware, Arduino Software | TBD |  |  | TBD | 

## Slide 4: Detailed Testing Plans: VFD Power and Spindle Speed
Chart: VFD Power Output vs. Spindle Speed
| 0 | 10.1 | 20.100000000000001 | 30.1 | 40 | 50.4 | 59.9 | 70.5 | 80.3 | 90.4 | 100
 | 0 | 591.6 | 1204.7 | 1808.2 | 2535.7 | 3029.4 | 3574.7 | 4228.1 | 4856.9 | 5325.5 | 6017.1
VFD (Hz) | Spindle (RPM)
0 | 0
10.1 | 591.6
20.1 | 1204.7
30.1 | 1808.2
40 | 2535.7
50.4 | 3029.4
59.9 | 3574.7
70.5 | 4228.1
80.3 | 4856.9
90.4 | 5325.5
100 | 6017.1

## Slide 5: Detailed Testing Plans: VFD Power and Spindle Speed

## Slide 6: Detailed Testing Plans: Speed vs Efficiency
Given stepper online torque vs speed curve, need to find our own
Cannot produce enough torque with given equipment therefore found speed vs efficiency
From stepper online:
  Input Wattage = 180 Watts
  Parasitic Loss = 9.6 Watts = 5% power consumption
In our graph we neglected the parasitic loss given we cannot supply 180 Watts
Reach peak efficiency ~ 40% which is similar to that of stepper online
Chart: Speed vs Efficiency (Stepper Online)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150
EFF (%) | 4 | 8 | 11 | 14 | 17 | 21 | 24 | 28 | 30 | 33 | 35 | 35 | 34 | 36 | 47

## Slide 7: Detailed Testing Plans: Input Power vs Efficiency
Chart: Input Wattage vs System Efficency
| 11.04 | 11.04 | 12 | 12.48 | 12.96 | 13.92 | 14.4 | 14.88 | 15.36 | 15.84 | 16.32 | 16.8 | 17.28 | 18.24 | 18.72 | 19.2 | 20.16 | 21.12 | 21.6 | 22.56 | 23.04 | 24.01 | 25.5 | 26.52 | 28.08 | 29.68 | 31.32 | 32.45 | 33.6 | 35.34 | 38.28 | 40.12 | 40.2 | 43.31 | 44.64 | 46.62 | 48.64 | 50.05 | 53.46 | 54.94 | 59.34 | 62.3 | 66.24 | 71.04 | 75.75 | 81.12
 | 0.014813 | 0.02751 | 0.039424 | 0.048808 | 0.072351 | 0.10023 | 0.076312 | 0.091448 | 0.061629 | 0.077019 | 0.16449 | 0.076107 | 0.095934 | 0.13673 | 0.14118 | 0.085986 | 0.12559 | 0.13938 | 0.15584 | 0.18554 | 0.18632 | 0.02319 | 0.075507 | 0.14095 | 0.21146 | 0.22086 | 0.20056 | 0.1957 | 0.1193 | 0.15783 | 0.21363 | 0.2073 | 0.092693 | 0.19639 | 0.19233 | 0.19093 | 0.19104 | 0.14486 | 0.17114 | 0.13182 | 0.17087 | 0.1505 | 0.15408 | 0.15843 | 0.18258 | 0.17687
Slope Equation:
If MAX wattage of the system is x = 192 W
  y = 0.436 = 43.6% Efficiency
Volts | Amperage | Input Power (W) | EFF (%)
48 | 0.23 | 11.04 | 1.48%
48 | 0.23 | 11.04 | 2.75%
48 | 0.25 | 12 | 3.94%
48 | 0.26 | 12.48 | 4.88%
48 | 0.27 | 12.96 | 7.24%
48 | 0.29 | 13.92 | 10.02%
48 | 0.3 | 14.4 | 7.63%
48 | 0.31 | 14.88 | 9.14%
48 | 0.32 | 15.36 | 6.16%
48 | 0.33 | 15.84 | 7.70%
48 | 0.34 | 16.32 | 16.45%
48 | 0.35 | 16.8 | 7.61%
48 | 0.36 | 17.28 | 9.59%
48 | 0.38 | 18.24 | 13.67%
48 | 0.39 | 18.72 | 14.12%
48 | 0.4 | 19.2 | 8.60%
48 | 0.42 | 20.16 | 12.56%
48 | 0.44 | 21.12 | 13.94%
48 | 0.45 | 21.6 | 15.58%
48 | 0.47 | 22.56 | 18.55%
48 | 0.48 | 23.04 | 18.63%
49 | 0.49 | 24.01 | 2.32%
50 | 0.51 | 25.5 | 7.55%
51 | 0.52 | 26.52 | 14.09%
52 | 0.54 | 28.08 | 21.15%
53 | 0.56 | 29.68 | 22.09%
54 | 0.58 | 31.32 | 20.06%
55 | 0.59 | 32.45 | 19.57%
56 | 0.6 | 33.6 | 11.93%
57 | 0.62 | 35.34 | 15.78%
58 | 0.66 | 38.28 | 21.36%
59 | 0.68 | 40.12 | 20.73%
60 | 0.67 | 40.2 | 9.27%
61 | 0.71 | 43.31 | 19.64%
62 | 0.72 | 44.64 | 19.23%
63 | 0.74 | 46.62 | 19.09%
64 | 0.76 | 48.64 | 19.10%
65 | 0.77 | 50.05 | 14.49%
66 | 0.81 | 53.46 | 17.11%
67 | 0.82 | 54.94 | 13.18%
69 | 0.86 | 59.34 | 17.09%
70 | 0.89 | 62.3 | 15.05%
72 | 0.92 | 66.24 | 15.41%
74 | 0.96 | 71.04 | 15.84%
75 | 1.01 | 75.75 | 18.26%
78 | 1.04 | 81.12 | 17.69%

## Slide 8: Detailed Testing Plans: Input Power vs Efficiency

## Slide 9: Detailed Testing Plans: Refined Joint Displacement
Goals of Testing
Preliminary Motor Movement
Control multiple motors in unison
Establish allowable range of motion for each joint to prevent
Future Work
Implement limit switches
Finetune code to reach precise location
Establish home position to which robot will return after operation

## Slide 10: Specification Sheets
Customer Requirement | CR met (Y/N) | Client Acceptable (Y/N)
CR 1 - Working Volume (50" D, 4' Height ) | Yes | 
CR 2 - 1/4" Aluminum Drilling | TBD | 
CR 3 - Human Input Responsive | Yes | 
CR 4 - .003" Drilling tolerance | TBD | 
CR 5 - Portable | Yes | 
CR 6 - Electric Power | Yes | 
CR 7 - Emergency Stop | TBD | 
CR 8 - Cost Efficient | Yes | 
Completion:
CR’s = 5/8 completed
  = 62.5 %

## Slide 11: Specification Sheets
Engineering Requirment | Target | Tolerance | Measured Value | ER met (Y/N) | Client Acceptable (Y/N)
ER 1 - Deflects < .1'' during drilling | .1'' | -.1'' |  | TBD | 
ER 2 - Spindle Speed 3000 Rpm | 3000 RPM | +/- 200 RPM | 3029.4 RPM | Yes | 
ER 3 - Motor Torque 100 N-m | 100 N-m | +/- 2 N-m |  | TBD | 
ER 4 - Human Input Responsive | Yes | N/A | N/A | Yes | 
ER 5 - Assembly < 150 lbs | 150 Lbs | +/- 10 Lbs | ~ 110 lbs | Yes | 
Completion:
ER’s = 3/5 completed
  = 60%

## Slide 12: Quality Function Deployment

## Slide 13: Assembly

## Slide 14: Detailed Testing Plans: Refined Joint Displacement
J4
J2