## Slide 1: NG Super Sonic Rocket PDR
Presenters: Austin Paothatat, Avery Charley, Koi Quiver,
Lindsey Dineyazhe

## Slide 2: Project Description
Our team is designing, building, and testing a two-stage supersonic rocket out of composite materials. The goal is to meet a set of advanced requirements that include an altitude of 40,000ft, maintain a speed of Mach 2, and carry a 10 lb. payload. The budget for this project is $7,000 plus any fundraising completed during the project.
Stakeholders
  Northrop Grumman
Avery 5/2/24 NG Super Sonic Rocket

## Slide 3: Engineering Requirements
Altitude of at least 40,000 ft AGL (Above Ground Level)
Required to carry a maximum 10 Lb payload
Require to reach and maintain over Mach 2 or roughly 1500 mph and maximize time spent at that speed or greater
Acceleration of the vehicle needs to meet a minimum of 12g's
Composite structural components will be simulated and tested to ASME standards
Current payload will carry instrumentation to measure vibrations during flight test and the ability to predict them
Recovery of entire launch vehicle for reuse
Koi 5/2/24 NG Super Sonic Rocket

## Slide 4: Functional Decomposition
Austin 5/2/24 NG Super Sonic Rocket

## Slide 5: CAD: Nose Cone
Lindsey 5/2/24 NG Super Sonic Rocket
Notes: Nose cone helps to reduce aerodynamic drag, control, and stability which helps with speed, acceleration, altitude, and fuel usage.

## Slide 6: CAD: Fins
Lindsey 5/2/24 NG Super Sonic Rocket
Notes: Controls direction and stability, also helps with speed, acceleration, and altitude.

## Slide 7: CAD: 2nd Stage Assembly
Koi 5/2/24 NG Super Sonic Rocket

## Slide 8: CAD: 2nd Stage Assembly
Koi 5/2/24 NG Super Sonic Rocket

## Slide 9: CAD: Booster Assembly
Koi 5/2/24 NG Super Sonic Rocket

## Slide 10: CAD: Sep System
Avery 5/2/24 NG Super Sonic Rocket
CLOSED
OPEN

## Slide 11: CAD: Sep System Parts 1/2
Avery 5/2/24 NG Super Sonic Rocket

## Slide 12: CAD: Sep System Parts 2/2
Avery 5/2/24 NG Super Sonic Rocket

## Slide 13: CAD: Motor Mount
Austin 5/2/24 NG Super Sonic Rocket

## Slide 14: CAD: Avionics
Austin 5/2/24 NG Super Sonic Rocket

## Slide 15: CAD: Full Launch Vehicle
Austin 5/2/24 NG Super Sonic Rocket

## Slide 16: CAD: Full Launch Vehicle
Austin 5/2/24 NG Super Sonic Rocket

## Slide 17: Engineering Calculations: Sep. System
Conditions of Separation
  Altitude = 9500 ft
  Velocity = 430mph (630.67ft/s)
Holding Strength:
  10.12lbf * 6 = 60.72lbf ≥ W1 = 13.01lbf
Assisted Separation Strength:
  F = -kx = -4.9lbf/in(-2.54in) 12.446lbf
  Number of Springs (3)  37.34lbf
Avery 5/2/24 NG Super Sonic Rocket
W = 48.53lbf
FD = 60.18lbf
Ff = 1586.81lbf
W = 13.01lbf
Ff = 857.76lbf
Upper Stage
Lower Stage
Sep. System

## Slide 18: Engineering Calculations: Nosecone
Lindsey 5/2/24 NG Super Sonic Rocket
387 K
γ = 1.4
Ma = 2
Fineness Ratio
Stagnation Temperature
Typical cure temperatures for carbon fiber pre-pregs ~ 250 °F or 350 °F, therefore a resin system that is cured at 350 °F would be preferred

## Slide 19: Engineering Calculations: Fin Drag
Koi 5/2/24 NG Super Sonic Rocket
Used the Drag Force formula:​
​
​
​
Variables:​
C_d = 0.005​
V = Mach 2 = 1535 (mph) = 686 (m/s)​
A = 26 (in^2) = 0.103226 (m^2)​
P = 8.80349*10^-2 (kg/m^3) = 0.0880349 (kg/m^3)​
​
Answer:​
D = 10.7 N = 2.403 (lbf) (Individual fin)​
D_tot = 10.7 N * 8 = 85.53 (N) = 19.23 (lbf) (total of all fins)​
​
Assumptions: Coefficient is of a flat plate at turbulent flow, the density of air is at an elevation of 20,000ft, the area used is the planform area. Some error due to compressiblility at Mach 2.​

## Slide 20: Engineering Calculations: Rocksim
Austin 5/2/24 NG Super Sonic Rocket

## Slide 21: Failure Mode Element Analysis
Avery 5/2/24 NG Super Sonic Rocket
Item # | Item | Failure | Root Cause | Likelihood 1 = least 5 = most | Severity 1 = least 5 = most | Precaution | Performance 1 = least 5 = most | Schedule 1 = least 5 = most | Cost 1 = least 5 = most
1.1 | Separation System (Staging) | Fails to Separate, buckling, thermal, | Electrical Failure, Mechanical failure | 3 | 5 | Ground Testing before launch to certify system | 1 | 3 | 3
1.2 | Separation System (Structural) | Failure in flight of sep. system, impact, thermal | System detaches mid-flight/ aero forces exceed limits | 2 | 4 | Ensure system is secured before flight. | 1 | 3 | 3
1.4 | Body (Structural) | Body bending, cracks, deformities | Forces during flight/temperature | 2 | 5 | Visual/NDT inspections | 2 | 2 | 3
1.5 | Fins (Structural) | Bending, cracks, deformities | Material deformation, adhesive epoxy failure | 2 | 5 | Visual/ NDT inspections | 2 | 2 | 3
1.6 | Avionics | Flight computers do not set off energetics | Battery failure, electrical short, match failure | 2 | 5 | Ground testing with energetics | 4 | 2 | 3

## Slide 22: Testing Procedures
Austin 5/2/24 NG Super Sonic Rocket
Structural Component Testing: Composite material strength testing, Separation system, Fin assembly.
  These components will be simulated and tested to ASME D638 and other applicable standards.
  Meets our structural testing requirement
Functionality Test of Systems: Avionics deployment, Separation system deployment, Payload ground testing
  All systems will be tested individually for this series of tests.
  Proves function of systems apart of the staging system and payload
Systems Test: Full dress rehearsal of the launch vehicle (Not including energetics)
  Proves launch vehicle is ready for flight and functions as expected
Subscale Testing: Built and tested subscale launch vehicle
  Further proves components and will be used for scale up data collection and improvements. This will be launched to collected data.
Full scale launch: Final launch vehicle will be constructed and ran through the testing procedures and complete a full flight.

## Slide 23: Bill of Materials
Koi 5/2/24 NG Super Sonic Rocket
BOM of the current vehicle design.
Most expensive parts:
  Motors
  Epoxy
  Carbon Fiber
  Raven Altimeters.
Account for about 93.1% of the total cost of the rocket
Projected the team will use 90% of the budget for the build of the rocket.

## Slide 24: Next Steps
Lindsey 5/2/24 NG Super Sonic Rocket
Wrap up Prototype 2
Analysis on designed components
Prototype revision and testing
Planning for next semester
Working over summer to develop the design.

## Slide 25: Conclusion
PHOTO
NG Super Sonic Rocket
Thank you!
Questions?