## Slide 1: NG Super Sonic Rocket
Presenters: Austin Paothatat, Avery Charley, Koi Quiver,
Lindsey Dineyazhe
Figure 1: Two stage rocket
University of Sheffield [1]

## Slide 2: Project Description
Our team is working towards building a two-stage supersonic rocket that will make use of advanced composite materials. Our foremost goal is to not only meet but surpass our customers’ expectations while keeping the budget under $7,300. Some important details to note are that we plan to conduct test flights in Fall 2024 and have a small-scale prototype ready by late April.
Stakeholders
  Northrop Grumman
Avery 2/26/24 NG Super Sonic Rocket

## Slide 3: Project Purpose
Provide launch vehicle for future capstone payload
Research and design a two-stage rocket capable of recording data
Provide a test bed for a future space shot rocket
Funding:
Northrop Grumman Space Systems, $7,300
Avery 2/26/24 NG Super Sonic Rocket

## Slide 4: Black Box Model
Avery 2/26/24 NG Super Sonic Rocket
Rocket
Flight
(2) Level 2 Motors
Midflight Separation
Carbon Fiber Material
Sustained Mach 2 Velocity
Max Altitude: 40,000+ ft.
10 lb. Payload

## Slide 5: Functional Decomposition
Austin 2/26/24 NG Super Sonic Rocket

## Slide 6: Concept Generations
Subsystems
  Avionics
  Separation System
  Body Design
  Fin Design
  Nose Cone
  Internal Rocket Layout
Requirements:
  5 concepts for each subsystem
Lindsey 2/26/24 NG Super Sonic Rocket

## Slide 7: Subsystem - Avionics
Austin 2/26/24 NG Super Sonic Rocket
A1
A2
A3

## Slide 8: Subsystem - Avionics
Austin 2/26/24 NG Super Sonic Rocket
A4
A5

## Slide 9: Subsystem – Separation System
Avery 2/26/24 NG Super Sonic Rocket
B1
B2
B3
B4
B5

## Slide 10: Subsystem – Body Design
Koi 2/26/24 NG Super Sonic Rocket
C1
C2
C3

## Slide 11: Subsystem – Body Design
Koi 2/26/24 NG Super Sonic Rocket
C4
C5

## Slide 12: Subsystem – Fin Design
Koi 2/26/24 NG Super Sonic Rocket
D1
D2
D3

## Slide 13: Subsystem – Fin Design
Koi 2/26/24 NG Super Sonic Rocket
D4
D5

## Slide 14: Subsystem - Nose Cone
Lindsey 2/26/24 NG Super Sonic Rocket
E1
E2
E3
E4
E5

## Slide 15: Subsystem – Internal Rocket Layout
Lindsey 2/26/24 NG Super Sonic Rocket
F1
F2
F3
F4
F5

## Slide 16: Designs Generated
Avery 2/26/24 NG Super Sonic Rocket
Design 1
Design 2
Design 3
Design 4
Design 5
Datum

## Slide 17: Pugh Chart
Concept Criteria | Design 1 | Design 2 | Design 3 | Design 4 | Design 5 | Design 6
Max Velocity | - (wide body, more drag) | + (aerodynamic) | - (high drag force) | S | S | datum
Separation Event | S | + | S | + | + | datum
Payload Capacity | -(unstable) | +(stable) | S | S | - | datum
Altitude | - | +(max velocity | - | S | S | datum
Lightweight | -(wide body) | +(less material) | - | S | - | datum
Cost of Production | -(more material) | +(less material) | - | S | - | datum
Reusable | S | S | S | S | S | datum
Payload Volume | - | - | + | S | - | datum
∑+ | 0 | 6 | 1 | 1 | 1 | N/A
∑- | 6 | 1 | 4 | 0 | 4 | N/A
∑s | 2 | 2 | 3 | 7 | 3 | N/A
Avery 2/26/24 NG Super Sonic Rocket

## Slide 18: Pugh Chart Results
Avery 2/26/24 NG Super Sonic Rocket
Design 2
Design 4
Design 5

## Slide 19: Decision Matrix
Criterion | Weight | Design 2 |  | Design 4 |  | Design 5 | 
 |  | Un-weighted score | Weighted score | Un-weighted score | Weighted score | Un-weighted score | Weighted score
Max Velocity | 30% | 100 | 30 | 90 | 27 | 95 | 28.5
Separation Event | 0% |  |  |  |  |  | 
Altitude | 25% | 100 | 25 | 90 | 22.5 | 95 | 23.75
Payload Weight |  |  |  |  |  |  | 
Lightweight | 15% | 85 | 12.75 | 70 | 10.5 | 80 | 12
Cost of Production | 15% | 95 | 14.25 | 75 | 11.25 | 90 | 13.5
Reusable | 10% | 95 | 9.5 | 95 | 9.5 | 95 | 9.5
Payload Volume | 5% |  |  |  |  |  | 
Total | 100% | Sum: | 91.5 | Sum: | 80.75 | Sum: | 87.25
Koi 2/26/24 NG Super Sonic Rocket

## Slide 20: Final Design
Koi 2/26/24 NG Super Sonic Rocket
Pros
Balanced weight distribution
Simple aerodynamic body
Simplified Avionics and Recovery systems
Easily manufacturable
Best performance

## Slide 21: Final Design - CAD
Koi 2/26/24 NG Super Sonic Rocket
Built in Solidworks

## Slide 22: Engineering Calculations: Magnetic System
Final Design includes Magnetic Separation System
Total Weight of lower half
  Carbon Fiber density (1550 kg/m^3)
  Carbon Fiber Body (r = 3in, 29.53in)
    1.111 kg
  Carbon Fiber Fins x 4 (8in x 6in)
    0.084 kg
  Level 2 Motor (~75mm)
    1-2 kg
  Avionics and Parachute
    1-2 kg
Final Total Weight: ~5kg/11.02lbs
Permanent Electromagnets [4]
  12mm Dia. And 12V connection
  Hold 3.3 lbs.
  Min: 4
Avery 2/26/24 NG Super Sonic Rocket

## Slide 23: Engineering Calculation: Rocket Fin Drag
Koi 2/26/24 NG Super Sonic Rocket
Used the Drag Force formula:
Variables:
C_d = 0.005
V = Mach 2 = 1535 (mph) = 686 (m/s)
A = 26 (in^2) = 0.01677 (m^2)
P = 8.80349*10^-2 (kg/m^3) = 0.0880349 (kg/m^2)
Answer:
D = 1.737 N = 0.390 (lbf) (Individual fin)
D_tot = 1.737N * 8 = 13.9 (N) = 3.125 (lbf) (total of all fins)
Assumptions: Coefficient is of a flat plate at turbulent flow, the density of air is at an elevation of 20,000ft, the area used is the planform area. Some error due to compressiblility at Mach 2.

## Slide 24: Engineering Calculations: Rocksim
Austin 2/26/24 NG Super Sonic Rocket

## Slide 25: Engineering Calculation: Fineness Ratio
Fineness ratio: The ratio of the length of a body to its maximum width or diameter
Helps reduce wave drag coefficient; but can increase skin friction drag
Generally, a high fineness ratio is wanted for supersonic speeds (~5:1)
Lindsey 2/26/24 NG Super Sonic Rocket
Notes: "At supersonic speeds, the fineness ratio has a significant effect on nose cone wave drag, particularly at low ratios; but there is very little additional gain for ratios increasing beyond 5:1. As the fineness ratio increases, the wetted area, and thus the skin friction component of drag, will also increase. Therefore, the minimum drag fineness ratio is ultimately going to be a trade-off between the decreasing wave drag and increasing friction drag."

## Slide 26: Budget Plans
PHOTO
Lindsey 2/26/24 NG Super Sonic Rocket
Funding:
1) Northrop Grumman - $7,300
2) Fundraising 10% - $730
  Material donations from Nova Kinetics
  GoFundMe
  Friends/Family Donations
  Potential fundraising collaboration w/Rocket Club
Budget | Description | Amount
Funding Available | Northrop Grumman | $7,300
Pending Expenses | Prototype rocket kit, prototype motors(x2) | ~$300
Anticipated Expenses | Avionics, RockSim Licenses, Rocket Certifications | $1000
Balance |  | $7,300

## Slide 27: Schedule (2/5 - 2/26)
Lindsey 2/26/24 NG Super Sonic Rocket

## Slide 28: Next Steps
Lindsey 2/26/24 NG Super Sonic Rocket
Report 1
Website
Prototype 1
  Ordering kit
  Building
  Launching
Continuing fundraising

## Slide 29: Conclusion
PHOTO
2/26/24 NG Super Sonic Rocket
Thank you!
Questions?

## Slide 30: References
PHOTO
  [1] A. Mishra, K. Gandhi, K. Sharma, N. Sumanth, and Y. Krishna. Teja, “CONCEPTUAL DESIGN AND ANALYSIS OF TWO STAGE SOUNDING ROCKET,” International Journal of Universal Science and Engineering, vol. 07, pp. 53–73, Aug. 2021.
  [2] P. Davies et al., “Preliminary Design and Test of High Altitude Two-Stage Rockets in New Zealand,” Aerospace Science and Technology, vol. 128, pp. 107741–107741, Sep. 2022, doi: https://doi.org/10.1016/j.ast.2022.107741.
  [3] P. Żurawka, N. Sahbon, D. Pytlak, M. Sochacki, A. Puchalski and S. Murpani, "Multi-Objective Optimization of a Fin Shape for a Passive Supersonic Rocket Stage," 2023 IEEE Aerospace Conference, Big Sky, MT, USA, 2023, pp. 1-12, doi: 10.1109/AERO55745.2023.10115859.
  [4] “EML12MM-12 - round permanent electromagnet 12 mm DIA. 12 volts DC - holding 3.3 lbs.,” APW Company, https://apwcompany.com/eml12mm-12/ (accessed Feb. 25, 2024).