## Slide 1: SAE Formula Chassis
Gustavo Ruiz
Brandon Guzman
Ryan Meger
Alexandra Brister
Carson Kent

## Slide 2: Project Description
Chassis Prototyping:
Aimed to be totally compliant with FSAE rule book:
  Aim for more comfort and spacious cockpit
  Improve on any discrepancies from last year's chassis.
  Start beginning early stages of prototyping
With PVC protype complete based on general constraints and goals of other sub teams, more self-directed learning can occur in preparation for later this semester or the beginning of next semester.
These skills will aid in the final fabrication of the chassis design
Figure 1: PVC prototype
Figure 2: Current CAD
GR

## Slide 3: Project Description
Integration w/ Other Sub-Teams
Better Handling
Driver Ergonomics
Manufacturing Constraints
Larger Front Hoop for Improved Dash
Lower Vertical COM (9.93”), Lighter Frame (61.1 lbs.), Aerodynamics
More Cockpit Room, Egress improvements
Source & Prepare Tubing, Build Jig, Weld
Structurally Safe Frame w/ Improved Handling
GR

## Slide 4: Decomposition Model
RM

## Slide 5: Concept Generation
CAD Prototype:
Aimed to be totally compliant with FSAE rule book
  Triangulation
  Spacing for driver
Main Changes from Last Years Chassis
  More cockpit room!
  Increased size of Front Hoop
  Made rear box 3 inches shorter
  Moved Pedal Box Farther Away
    Allows for more adjustability
RM
Main concept generations:
  Aero design (several nose cones)
  Seat designs (seats, seat belt straps, steering wheel etc.)

## Slide 6: Concept Generation
RM
Chassis Style (1) Worst – (5) Best | Monocoque(Carbon) | Space-frame | Hybrid(semi-monocoque)
Weight | 5 | 2 | 4
Cost | 2 | 5 | 3
Durability | 3 | 4 | 4
Manufacturability | 1 | 5 | 2
Strength | 5 | 3 | 4
Total | 16 | 19 | 17

## Slide 7: Concept Generation (Aero)
PHOTO
PHOTO
CK
Chosen airfoil geometry for wings
Simple front wing design (not efficient)
Split front wing design (more efficient, easier to mount)
Nose cone design #1
Nose cone design #2

## Slide 8: Engineering Calculations (Alexandra)
Stress for 6-Point Seat Belt

## Slide 9: Engineering Calculations (Alexandra)
Safety Factor for 6-Point Seat Belt

## Slide 10: Engineering Calculations- Force Analysis
RM
)
Y
X
Target/Benchmark value =2400 Nm/deg
Theoretical Forces:
Estimation of Force:
m = 225 kg
a = 2g
4414.5 N
Torsional Analysis (Ryan Meger)
Frame Design was based off last years and was made in SolidWorks over the summer. No indication for making major design changes were mentioned. Analysis on current design was done.

## Slide 11: Engineering Calculations- Force Analysis
RM
Calculated Theoretical CT= 1932.7 Nm/deg
Torsional Analysis (Ryan Meger)
Displacement Plot
FOS Plot
FOS = 2.6
Stress Plot

## Slide 12: Engineering Calculations
Front Impact
PHOTO
PHOTO
Front View:
Side View:
Stress Plots
RM

## Slide 13: Engineering Calculations
Side Impact
PHOTO
PHOTO
Top View:
Isometric View:
Same amount of Force = 25,000 N
Stress Plots
RM

## Slide 14: Early Prototype Practice:
Early fabrication practice includes:
Steel tube bending
  This consisted of an early prototype of the front hoop for the 25' car using leftover Size B steel tube.
  Spring-back of steel was also practiced during the duration of this prototyping.
Hole sawing
  Early practice making cuts for final design, as well as for another team member to practice tacking.
BG
Figures: Front hoop Prototype
Figures: Hole saw practice & tacking

## Slide 15: Engineering Calculations
Equations: (Brandon Guzman)
PHOTO
Steel bending calculations:
Simple calculations for finding length of steel tube for bending.
Consisted of use of Solid works for angles, and mathematical hand calculations to find length.
Bending Constant:
Constant = 0.01745
Equation:
For r1:
For r2:
Figure: Front hoop drawing & angles
[1]“The construction Process: Pipe and Tube bending,” https://www.herl.pitt.edu/indiachair/indiachairsh/cl_bend.html#:~:text=Rule%20for%2090%20d (accessed Oct. 2, 2024)

## Slide 16: Evaluation of Prototype Practice
Key Takeaways & Errors:
Learning to use hydraulic bending chuck
Learning to bend steel tube and adjust for spring-back
Grasp the use of angle gauge for precise bends
Team needs to source a 4" bending chuck to fit CAD design. Current front hoop used 3" benching chuck, which caused some misalignment with the one-to-one scale drawing.
Figure: Front hoop Prototype

## Slide 17: Engineering Calculations (Aero)
PHOTO
PHOTO
CK
Pressure plot for angle of attack of –30 degrees
Lift and drag results
Preliminary calculations were performed on the chosen airfoil geometry using the vortex panel method
Results are promising as pressure spikes on the leading edge of the airfoil and decreases down the chord
Negative lift results in downforce, so a coefficient of lift of –3 tells us at a –30 degree angle of attack we will produce significant downforce

## Slide 18: Concept Evaluation
Weight Table | 
Weight | 0.25
Strength | 0.2
Safety | 0.2
Manufacturability | 0.15
Integration | 0.1
Handling | 0.1
Scale 1-5 | 2024 Frame | 2025 Frame
Weight | 3 | 4
Strength | 4 | 4
Safety | 4 | 5
Manufacturability | 3 | 4
Integration | 3 | 5
Handling | 3 | 4
TOTAL | 3.4 | 4.3
Decision Matrix
GR

## Slide 19: Schedule
Gantt Chart
GR

## Slide 20: Schedule
Complete PVC Frame
Complete JIG Design
Source JIG Materials
Prepare Tubing for JIG
Weld
Fill out SES as we go
GR

## Slide 21: Budget
Budget can range from $4k-7K depending on Aerodynamics
GR

## Slide 22: Bill of Materials for JIG
JIG BOM |  |  | 
Part | Units | $/Unit | Total
MDF Board (3/4"x 4'x 8') | 3 | $48.98 | $146.94
Angle Iron (1/8" x 2" x 48") | 1 | $32.47 | $32.47
Washers (3/16" x 1.5") | 1 | $8.62 | $8.62
Bolts (M8-1.25x40mm class 8.8) | 40 | $2.75 | $110.00
Nuts (M8-1.25 2 per bag) | 20 | $1.25 | $25.00
Screws 140 pack (8 x 1.25") | 1 | $13.37 | $13.37
 |  |  | $336.40
GR

## Slide 23: Sources:
GR
Ryan Meger:
[1] N. Geneva and C. Dodd, “Meeg 402-010 chassis design report 2017 FSAE SENIOR ...,” MEEG 402-010 Chassis Design Report, https://udel.edu/~pgeneva/downloads/fsae/2017_FSAE_chassis.pdf (accessed Oct. 8, 2024).
[2] D. Milliken and W. Milliken, “Race Car Vehicle Dynamics,” SAE International, https://www.sae.org/publications/books/content/r-146/ (accessed Oct. 8, 2024).
[3] Formula Team, “1st Year Final Report.” NAU, Flagstaff, May. 1, 2024
[4] FSAE, “2024 Formula SAE Rule Book,” Formula SAE, https://www.fsaeonline.com/cdsweb/gen/documentresources.aspx (accessed Oct. 8, 2024).
[5] R. Patil, “FEA analysis of FSAE chassis,” FEA Analysis of FSAE Chassis , https://www.ijert.org/research/fea-analysis-of-fsae-chassis-IJERTV9IS070148.pdf (accessed Oct. 8, 2024).

## Slide 24: Thank You!